## Slide 1
Introduction to the
Clinical Laboratory
Chapter 45

## Slide 2: Clinical Laboratory
Discuss the role of the clinical laboratory personnel in patient care and the medical assistant’s role in coordinating laboratory tests and results.
Describe the divisions/departments of the clinical laboratory.
Explain the three regulatory categories established by the Clinical Laboratory Improvement Amendments (CLIA), and identify CLIA-waived tests associated with common diseases.
Identify quality assurance practices in healthcare, document the results on a laboratory flow sheet, and discuss quality control guidelines.

## Slide 3: Clinical Laboratory
Discuss laboratory safety and the governing agencies involved in safety standards.
Discuss the purpose of a Safety Data Sheet (SDS), and summarize safety techniques to minimize physical, chemical, and biologic hazards in the clinical laboratory.
Describe the essential elements of a laboratory requisition.
Discuss specimen collection, including the importance of sensitivity to patients’ rights and feelings when collecting specimen. Also, discuss the eight steps to follow when collecting specimens and informing patients of their results.

## Slide 4: Clinical Laboratory
Explain the chain of custody and why it is important.
Discuss the measurement of time and temperature, and name the metric units used for measuring liquid volume, distance, and mass.
Name the parts of a microscope, and describe their functions. Also, summarize selected microscopy tests that may be performed in the ambulatory care setting.
Describe the safe use of a centrifuge.
Discuss the use of an incubator.

## Slide 5: Personnel in the Clinical Laboratory
Laboratory tests are an essential part of a medical diagnosis
Personnel may include:
  A director (who may be a pathologist)
  Certified medical technologists (MTs) and certified medical laboratory technicians (MLTs)
  Medical laboratory assistants (MLAs)
  Credentialed medical assistants (CMAs and RMAs)
  Phlebotomists
Notes: In a clinical laboratory, a medical assistant is trained to perform certain testing procedures and in methods of collecting specimens that are sent to outside reference laboratories for testing.
To assume this responsibility, you must know proper patient preparation, the procedures for each test, and the normal range of results for the test.
The agencies granting certifications and titles are listed in Table 45.1 in the textbook.

## Slide 6: Laboratory Tests
Four main purposes:
  To document the good health of a patient
  To screen patients for diseases such as diabetes, high cholesterol, or urinary tract infections (UTIs)
  To help the provider diagnose a medical disease, disorder, or condition
  To help the provider decide the most appropriate treatment, to monitor the effects of medications and treatments, and to monitor a disease process
Notes: Only healthcare providers can request laboratory testing for a patient.
Medical assistant must carefully follow all laboratory instructions.

## Slide 7: Clinical Laboratory Testing
Used with a thorough health history and physical exam to obtain essential data for diagnosis and management of patient’s condition
Abnormal test results can indicate more than one pathologic condition, so more information is needed
Screening tests examine a particular specimen for presence of a substance that may indicate a disease, often qualitative
Quantitative tests measure numeric values with a unit, such as analyte per given volume
Notes: What information can a screening test provide? Provide an example. (These types of tests are not diagnostic for any particular disease, but rather indicate that the disease state may exist. Screening tests are done routinely on patients on the basis of their age, history, or gender. The fecal occult blood test for hidden or microscopic blood in the stool is an example of a screening test. Blood is not normally found in the stool, and its presence may indicate a cancerous lesion in the colon, but further tests will be needed.)
Refer to Table 45.2 in the textbook for a comparison of qualitative and quantitative testing.

## Slide 8: Departments of the Clinical Laboratory
Urinalysis
  Physical, chemical, and microscopic evaluation of urine
Hematology
  Study of blood cells and coagulation
Chemistry
  Analyzes chemicals found in blood, cerebrospinal fluid, urine, and joint fluid
Microbiology
  Involves the study of bacteria, fungi, yeasts, parasites, and viruses
Notes: Large laboratories may include other departments like blood bank, coagulation, serology, cytology, and special chemistry.
In the microbiology laboratory, microorganisms are grown from blood, urine, sputum, cerebrospinal fluid, and wound specimens and are identified under the microscope.

## Slide 9: Urinalysis
Physical, chemical, and microscopic examination of urine
  Physical includes color, clarity, specific gravity
  Chemical measures levels of glucose, protein, ketones, blood, bilirubin, urobilinogen, nitrites, and pH
  Microscopic looks for certain cells, mucus, casts, crystals, yeasts, parasites, and bacteria
  **this information is crucial!!
Notes: Additional quantitative tests may be performed in the urinalysis department to confirm routine screening tests.

## Slide 10: Hematology
Study of blood cells and coagulation
Qualitative or quantitative
  Blood cell counts determine exact number of RBCs or erythrocytes, WBCs or leukocytes, or platelets (thrombocytes)
  Qualitative tests determine characteristics of cells, such as size, shape, and maturity
Notes: In addition, the hematology department performs tests to determine the coagulating ability of blood components.

## Slide 11: Chemistry and Microbiology
Chemistry analyzes blood, cerebrospinal fluid (CSF), urine, and joint fluid (synovial fluid)
Microbiology involves study of bacteria, fungi, yeasts, parasites, and viruses
  Microorganisms are grown from specimens and identified
Notes: Specimens for microbiology must be collected aseptically in sterile containers.
The goal of the microbiology department is to identify the microorganism that is causing the infection.

## Slide 12: Clinical Laboratory Improvement Amendments (CLIA)
Established quality standards for all laboratory testing to ensure accuracy, reliability, and timeliness of patient results
Three regulatory categories:
  Waived tests
  Moderate-complexity tests
  High-complexity tests
Notes: CLIA requires that all entities that perform even one test, including waived tests, must meet certain federal requirements and must register as a laboratory.
Certain tests have been approved for home use and are considered waived tests, meaning that they are exempt from CLIA.
Refer to the unnumbered box in the textbook titled “Common Government Acronyms in the Clinical Laboratory.”
Table 45.3 in the textbook outlines CLIA-waived tests and their purposes.

## Slide 13: Moderate- and High-Complexity Tests
Laboratories that perform these tests must meet CLIA regulations and are subject to unannounced inspections every 2 years
Must establish a system to maintain integrity and identification of patients’ specimens throughout testing process and to ensure accurate reporting of results
Medical assistants may perform all CLIA-waived tests and some moderately complex tests, depending on the certification of the laboratory or POL in which they are employed
Notes: CLIA program oversees the quality of nearly 200,000 different laboratory procedures.
Although you may not perform high-complexity tests, you may often be involved in collecting the specimens required, preparing the patient for the test, and recording the results in the medical record.

## Slide 14: Quality Assurance (QA) Guidelines
QA encompasses a comprehensive set of policies developed to ensure excellent documentation and reliability of laboratory testing
  Also focuses on establishing a series of operating procedures for the benefit of the patient and the medical assistant doing the laboratory testing
  Process is divided into three stages:
    Preanalytic
    Analytic
    Postanalytic
Notes: QA is a set of written policies and procedures that ensure the monitoring of all the processes involving before, during, and after a laboratory test is performed in order to produce reliable patient test results.
Accurate record keeping is one of the key responsibilities of the medical assistant.
If any of these steps in any of these three stages are missed or performed incorrectly, QA has been broken.
Figure 45.1 in the textbook shows the checklist summary of the steps needed to ensure proper CLIA-waived testing in a POL.

## Slide 15: Quality Control (QC) Guidelines
Specially prepared QC samples are tested daily, along with patient samples
Objective of QC in the laboratory is to ensure the reliability of the test results
On every day that patient tests are performed, QC tests must also be performed and the results entered on the flow sheet
KNOW THIS!!!
Notes: Accurate record keeping is one of the key responsibilities of the medical assistant.
Refer to Procedure 45.1 in the textbook to perform a quality control measure on a glucometer and record the results on a flow sheet.
Discuss some quality control examples—see the unnumbered box in the textbook.
Discuss preventive maintenance programs for laboratory equipment—see the unnumbered box in the textbook.

## Slide 16: Laboratory Safety Standards
Safety standards for laboratories are initiated, regulated, and reviewed by several agencies or committees
OSHA mandates two programs for safety in laboratories
  One covers occupational exposure to chemical hazards
  One covers exposure to blood-borne pathogens
Notes: What are some of the government regulatory bodies over laboratory safety? (These include the U.S. Department of Labor’s Occupational Safety and Health Administration [OSHA]; the Clinical and Laboratory Standards Institute [CLSI]; the Centers for Disease Control and Prevention [CDC], an agency of the U.S. Department of Health and Human Services; the College of American Pathologists [CAP]; and the Environmental Protection Agency [EPA].)

## Slide 17: Laboratory Safety
U.S. government created a system of safeguards and regulations under the Occupational Safety and Health Act of 1970
CDC also has established recommendations and resources in Standard Precautions and Transmission Precautions
Notes: The importance of safety in the laboratory cannot be overemphasized.

## Slide 18: Chemical Hazards
Identification of the product
Hazard(s) identification
Composition/information on ingredients
First-aid measures
Fire-fighting measures
Accidental release measures
Handling and storage
Exposure controls/ personal protection
Physical and chemical properties
Stability and reactivity
Toxicologic information
Ecologic information
Disposal considerations
Transport information
Regulatory information
Other information
Notes: The clinical laboratory is home to chemicals that are flammable, caustic, poisonous, carcinogenic, and/or teratogenic.
What does OSHA recommend for each Safety Data Sheet (SDS)? (OSHA recommends that each SDS follow the 16-section format developed by the American National Standards Institute [ANSI]. When this format is used, information about the hazardous material that affects the worker the most is identified at the beginning of the form and the more technical information about the product is given later.)
Please note that Sections 12-15 are regulated by agencies other than OSHA and are required of the manufacturers, not the employees.

## Slide 19: Chemical Safety Procedures
Never pipet by mouth
Work under fume hood
Rinse exposed skin under water for 5 minutes
Use eyewash station for at least 15 minutes
Keep chemicals tightly sealed and know hazard identification symbols
Notes: What do the chemical hazard identification symbols mean? (The top diamond is red and indicates a flammability hazard. The diamond on the left is blue and indicates hazards to health. The bottom diamond is white and provides special hazard information, including radioactivity, special biohazards, and other dangerous situations. The diamond on the right is yellow and indicates a reactivity or stability hazard.)
Refer to Figures 45.2 and 45.3, as well as Procedure 45.2, in the textbook.

## Slide 20: Biologic Hazards and Infection Control
Biohazards are materials or situations that present risk or potential risk of infection
Potentially infective specimens include blood, body tissue biopsy specimens, urine, exudates, and bacterial cultures and smears
Label potentially biohazardous material
Notes: The OSHA-mandated program, Occupational Exposure to Bloodborne Pathogens, must be in place.
How can infection occur? (Infection can occur through aspiration of a pathogen, accidental inoculation by a needlestick, aerosols created by uncapping specimen tubes, centrifuge accidents, and entry of pathogens through cuts and scratches.)
Refer to Figure 45.4 in the textbook.

## Slide 21: Standard Precautions
Bloodborne Pathogens Standard (BBPS) covers all employees who could reasonably be exposed to infectious material while doing their job
Laboratory employer must have a written exposure control plan
Urine is the only body fluid not specifically included in the BBPS standard
Notes: Hepatitis B virus (HBV), hepatitis C virus (HCV), and human immunodeficiency virus (HIV) are a constant threat to the health and safety of clinical laboratory personnel.
Blood and body fluids are the primary substances handled in the laboratory.
Standard Precautions include the following five elements: hand hygiene, use of PPE, safe needle practice, safe handling of potentially contaminated equipment or surfaces in the patient environment, and respiratory hygiene/cough etiquette.

## Slide 22: Washing and Sanitizing the Hands
When entering and before leaving the area
Before and after every patient procedure
After contact with body fluid, even if gloves were worn
Before and after eating
Before and after using the restroom
Notes: What is the most effective means of preventing infection? (Washing or sanitizing the hands is the most effective means of preventing infection.)
Every laboratory should have a safety manual that covers all safety practices and precautions.

## Slide 23: Bloodborne Pathogens Standard
Regulates the handling of blood and blood products, as well as other potentially infectious materials (OPIM)
Covers all employees who could “reasonable anticipate contact with blood and other potentially infectious materials as a result of performing their job duties”
Requires that laboratory employer has a written exposure control plan
Notes: Has been law since 1992.

## Slide 24: Safety Guidelines for Other Potentially Infectious Materials (OPIM)
Handle and process all specimens as if they contain infectious material
Wipe the outside of specimen containers with a germicide
Dispose of all infectious materials according to state and federal guidelines
Clean up spills using a disinfectant
Immediately dispose of any chipped or broken glassware into a sharps container using appropriate safety methods to prevent accidental punctures
Notes: Has been law since 1992.

## Slide 25: Physical Hazards
Electrical
Fire
Mechanical
Notes: Use surge protectors.
Inspect all cords frequently.
Never use extension cords.
Do not overload circuits.
Flammable materials should not be stored near any source of ignition.
Fire safety blankets should be used to smother flames on burning clothing.
Emergency phone numbers should be posted on the wall near the phone.
Special care should be exercised when using equipment with moving parts.
Refer to Figure 45.6 and Procedure 45.3 in the textbook.

## Slide 27: Laboratory Requisitions and Reports
Various methods are used to file laboratory reports in a patient’s medical record
Make sure that all reports are received for diagnostic tests performed on the patient outside the physician’s office
Only file reports after the physician has reviewed the results
Written requisitions for outside tests must be sent to the laboratory
Notes: Describe written requisition forms. (These forms are preprinted, and the most commonly requested tests are indicated in logical sequence. Patient information must be complete, accurate, and legible.)
Refer to Figure 45.7 in the textbook to see a sample of an electronic laboratory requisition form.

## Slide 29: Specimen Collection
Most common specimens: Blood, urine, and swab samples collected from wounds or mucous membranes
Less often: Feces, gastric contents, CSF, tissue samples, semen, and aspirates, such as synovial fluid
Notes: Why is the collection of specimens such an important duty for a medical assistant? (It is important to recognize that all clinical laboratory results are only as good as the specimen received. The importance of specimen collection cannot be overemphasized. If test results are to be accurate indicators of the patient’s state of health, it is imperative that the concepts of specimen collection be understood and followed exactly.)
Using a minimum of two patient identifiers before specimen collection is standard.

## Slide 30: Ensuring Accuracy
Initial identification of the patient is essential
Collect the specimen in an appropriate collection container
Color-coded tubes or sterile specimen containers may be used
Notes: If the patient is to collect the specimen at home, he or she should be provided with the appropriate container and complete instructions for collection.
Refer to Figure 45.8 in the textbook to view color-coded tops.

## Slide 31: Labeling Specimens
Provider’s name, account number, address, and phone number
Patient’s full name, age, date of birth, gender, address, and insurance information
Source of specimen; date and time of collection
Specific test (or tests) requested; medications patient is taking
Whether patient fasted or followed dietary restrictions if required; time of last intake
Possible diagnosis
Indication of whether test is to be performed stat
Notes: Always check the laboratory’s specimen requirements manual for any unfamiliar tests.
The container must be labeled properly at the time of collection; unlabeled containers will not be accepted for laboratory testing.

## Slide 32: Preventing Contamination
Expiration dates on swabs, tubes, transport media, and other collection containers should be checked before these items are used
Sufficient samples should be collected for tests requested by physician
The specimen collected must be a true representative sample
Notes: All blood and other body fluids from all patients should be considered infectious.
What does a "true representative sample" mean? (For example, a swab for a wound culture collected from the surface of the wound generally does not yield the same results as one taken from the depths of the wound. A hemolyzed blood specimen, or one taken from an atypical area, such as a hematoma or the area above or below an intravenous drip, shows marked differences in many tests.)
Refer to Figure 45.9 in the textbook.

## Slide 33: Handling, Processing, and Storing Specimens
Specimen must be handled, processed, and stored according to individual guidelines
Determine whether the specimen needs to be kept warm or cool
Laboratory specimen requirements should be consulted to ensure that each specimen is handled and processed properly
Notes: What are some examples of tests that require special conditions for storage? (Answers will vary but may include the following: Samples for gonorrhea cultures and semen analysis are two such examples because cooling kills microorganisms and sperm. When required, serum must be separated from the cells as soon as possible after the specimen has clotted to prevent changes caused by the metabolism of the cells. Specimens for bilirubin testing must be protected from light.)
Serum must be separated from RBCs as soon as possible after the specimen has clotted to prevent changes caused by the metabolism of the blood cells.

## Slide 34: Chain of Custody
When a specimen is evidence in court case, certain procedures must be followed in collecting and handling
Specimen processing must be documented meticulously
Chain of custody refers to the stepwise method used to collect, process, and test a specimen
Documentation must be signed by every person who has contact with the specimen, from collection to the final reporting of results
Notes: You could potentially be subpoenaed to testify in court about specimens collected; therefore, it is in your best interest to follow chain of custody procedures rigorously.

## Slide 35: Measuring Time
Time of day often is a critical factor in patient care
Many facilities use military time, based on four digits in terms of “hundred hours”
Noon is 1200, midnight is 0000 or 2400
Based on 60-minute hours
Notes: Refer to Table 45.4 in the textbook.
Express 5:35 pm in military time. (1735)
Express 2:40 am in military time. (0240)

## Slide 36: Measuring Temperature
Fahrenheit scale
  Part of the English system of measurement; most commonly seen in United States
Celsius scale
  Used in countries that apply the metric system
Notes: Refer to Table 45.5 in the textbook.
Almost all laboratories in the United States use Celsius scale for temperature.
Convert temperatures between the two scales.

## Slide 37: Units of Measurement
Metric system and Système International (SI) are used in the laboratory
Basic units for metric system are gram (g) for weight, meter (m) for length, and liter (L) for volume
Some common units for reporting analytes are mg, µ, g, dL, and L
SI system is an adaptation of metric system
Notes: It is very important that you double-check the laboratory’s standard and include the appropriate units of measurement when reporting test values.
Refer to Tables 45.6 through 45.8 in the textbook.

## Slide 38: Measuring Liquid Volume
Test tubes come in many sizes and are typically disposable
Micropipets are used to deliver very small amounts of liquid
Tips may be sterile
Notes: It is important to follow the manufacturer’s instructions for the device because each may be slightly different.
Refer to Figures 45.10 and 45.11 in the textbook.

## Slide 39: Microscope
Used to view objects too small to be seen with the naked eye
Used to evaluate stained blood smears, urine sediment, vaginal secretions, and smears made from body fluids and microorganisms
Notes: Refer to Figure 45.12 in the textbook.

## Slide 41: CLIA-Approved Procedures for Provider Performed Microscopy (PPM)
Direct wet mount
KOH preparation
Fecal leukocyte examination
Pinworm examinations
Postcoital direct, qualitative examinations
Qualitative semen analysis
Urine sediment examination
Notes: Refer students to Table 45.9 for a list of microscopy tests, their descriptions, and examples of each.

## Slide 42: Microscope Use and Maintenance
Microscopes have three components
  Magnification system
  Illumination system
  Framework
Must be kept scrupulously clean at all times
Should be placed in a permanent location in the laboratory on a sturdy table in an area where it cannot be bumped
Notes: The microscope is focused through movement of the objective or stage, which is controlled by round knobs on both sides of the microscope.
Refer to Procedure 45.4 in the textbook for the steps to using the microscope and performing routine maintenance on clinical equipment.

## Slide 43: Centrifuge
Used when solids must be separated from liquids
Involves the application of increased gravitational force achieved by rapid spinning
Directions for using the centrifuge are usually given in terms of revolutions per minute (rpm)
Dangerous if used incorrectly
Notes: What are some examples of samples that may require centrifugation? (Centrifugation is used to separate blood cells from serum and also solid materials, such as cells and crystals, from urine.)
How do you load the centrifuge for safe use? (The most important rule is to ensure that the centrifuge is balanced so that tubes of equal size and containing equal volume are directly across from one another in the rotor holders. Tubes being centrifuged should be capped to prevent emission of aerosols. Rubber cups should be placed in the bottom of the carrier cups to prevent breakage of glass tubes. Centrifuges should never be opened while they are in operation.)
Refer to Figure 45.13 in the textbook.

## Slide 45: Incubator
Cabinets that maintain constant temperatures
Generally used in microbiology laboratory
Usually have warning alarms if temperature exceeds or falls below specified range
Temperature should be checked daily
Notes: Refer to Figure 45.14 and Table 45.10 in the textbook.

## Slide 46: Patient Coaching
For many testing procedures, patients must be given a specific set of instructions to follow
You may be responsible for explaining to the patient measures to be taken before laboratory testing
Make sure you have interpreted the physician’s orders correctly
Patient should be given written instructions
Notes: Be sure a phone number is included on the instruction sheet so the patient can call if he or she has questions.

## Slide 47: Legal and Ethical Issues
Use common sense and document everything
Make sure the physician has reviewed and signed the test results and has given permission for the patient to be told the results
Maintain confidentiality when disclosing test results
Notes: If you are aware of a potential safety problem, report it to the person in charge.
Your welfare, the welfare of the patient, and the welfare of your co-workers may depend on your commitment to safety.

## Slide 48: Patient-Centered Care
Risks to laboratory workers can be greatly reduced when everyone who works in laboratory is conscious of safety guidelines
Remember: If it hasn’t been documented, it never happened
Your welfare, the welfare of patient, and the welfare of coworkers may depend on your commitment to safety