## Slide 1
Surgical Supplies and Instruments
Chapter 24

## Slide 2: Surgical Supplies and Instruments
Describe typical solutions and medications used in minor surgical procedures.
Summarize methods for identifying surgical instruments used in minor office surgery, and then identify some surgical instruments.
Outline the general classifications of surgical instruments.
Identify drapes and different types of sutures and surgical needles.
Describe the care and handling of surgical instruments.

## Slide 3: Minor Surgery Room
Changing room and minor surgery room separate from other examination rooms
Should be near a workroom with a sink and autoclave
Should be easy to disinfect and uncluttered
Operating table, clock, operating light, sitting stools, and Mayo stands
Cabinets (that store supplies) with countertops
Notes: Supplies used in this room should not be used elsewhere, and supplies used elsewhere should not be brought into this room.
Refer to Figure 24.1 in the textbook to see a typical surgical procedure room in an ambulatory care setting.

## Slide 4: Surgical Solutions and Medications
Responsible for care and maintenance of supplies
  Sterile water (multiple-dose or single-use vials)
  Sterile normal saline solution
  Surgical scrub preparations like chlorhexidine and Betadine
  Anesthetics, formalin solution, and specimen bottles
  Topical silver nitrate to stop bleeding
Notes: Although the solutions and medications listed here are basic, every physician’s office practice has preferred items and methods of applying them.
Surgical scrub preparations should:
  Be effective against bacterial spores
  Work to reduce transient bacteria
  Show evidence of persistent activity on the skin
  Work despite the presence of organic matter, such as blood or wound drainage

## Slide 5: Surgical solutions and medications
Medical assistant is responsible for accurately labeling specimen containers with:
  Patient’s name and date of birth
  Medical history number
  Date of collection
  Type of specimen
Notes: Sometimes the provider may want to use a topical silver nitrate solution or coated applicator sticks to stop localized bleeding.

## Slide 6: Additional Surgical Supplies
Sterilized gauze squares or strips saturated with petroleum jelly or petrolatum
Sterilized iodoform gauze strips
Surgical sponges
Syringes and needles
Sterile dressing and bandaging materials
Notes: Refer to Figure 24.2 in the textbook to see gauze strips.

## Slide 7: Surgical Instruments
Know which instruments are used for each procedure, and be able to identify and understand the function of surgical instruments preferred by the physician
Instruments have clearly identifiable parts and can be visually differentiated
  Components are the handle, closing mechanism, and the part that comes in contact with patient, commonly called the jaws
Notes: Many instruments can be ordered with either straight or curved tips, depending on the operator’s preference and the task to be performed.
Procedure 24.1 describes how to wrap surgical instruments and supplies for sterilization in an autoclave.
Refer to Figures 24.3 through 24.5 in the textbook to view ring-handle forceps, spring-handle forceps, instruments with serrations, toothed jaws, and teeth of Allis tissue forceps.

## Slide 8: Classifications of Surgical Instruments
Generally classified according to their use:
  Cutting
  Grasping
  Retracting
  Probing and dilating

## Slide 9: Cutting and Dissecting Instruments
Bandage scissors
Operating (surgical) scissors
Littauer stitch or suture scissors
Disposable scalpels
Notes: Refer to Table 24.1 in the textbook to discuss scissors.
Refer also to Figures 24.6 through 24.8 in the textbook to see Lister bandage scissors, operating scissors, suture scissors, and disposable scalpels.
Most scalpels used in minor procedures are disposable. Once used, disposable scalpel/blade units are discarded in a sharps container.

## Slide 10: Grasping and Clamping Instruments
Hemostat forceps
Needle holders
Splinter forceps
Adson forceps
Plain thumb (dressing) forceps
Towel forceps
Allis tissue forceps
Foerster sponge forceps
Transfer forceps
Adson thumb forceps
Bayonet forceps
Plain-tip tissue forceps
Toothed tissue forceps
Notes: Clamping instruments are used for many different tasks.
Refer to Figures 24.9 through 24.13, as well as Table 24.2, in the textbook.

## Slide 11: Retractors
Hold tissue away from surgical wound incision
Handheld skin hooks or Senn retractors based on provider’s preference
Senn retractor
  Flat end is blunt retractor
  Three-prong end may be sharp or dull
  Used to retract small incisions or to secure a skin edge for suturing
Notes: Refer to Figure 24.14 in the textbook to see a Senn retractor.

## Slide 12: Probes and Dilators
Probes
Trocars and obturators
Specula
Nasal specula
Notes: What are the purposes of probes and dilators? (Probes and dilators are used for both surgery and examinations. Probes can be used to search for a foreign body in a wound or to enter a fistula. Dilators are used to stretch a cavity or opening for examination or before inserting another instrument to obtain a tissue specimen.)
Refer to Figures 24.15 and 24.16, as well as Table 24.3, in the textbook.

## Slide 13: Gynecologic Instruments
Placenta forceps
Endocervical curette
Sims uterine curette
Schroeder uterine vulsellum forceps
Hegar uterine dilators
Sims uterine sounds
Notes: The medical assistant must organize and set up the instruments needed for each particular examination in what is called a tray setup.
Refer to Table 24.4 in the textbook, as well as Figures 24.17 and 24.18.

## Slide 14: Ophthalmologic and Otolaryngologic Instruments
Krause nasal snare
Metal tongue depressor
Hartmann “alligator” ear forceps
Laryngeal mirror
Ivan laryngeal metal applicator
“Buck” ear curette
Sharp ear dissector
Wilde ear forceps
Notes: Another specialty grouping of instruments is ophthalmologic and otolaryngologic instruments.
Refer to Table 24.5 in the textbook, as well as Figures 24.19 and 24.20.

## Slide 15: Biopsy Instruments
Cervical biopsy forceps
Rectal biopsy punch
Silverman biopsy needle
Notes: Refer to Table 24.6 in the textbook, as well as Figure 24.21.

## Slide 16: Genitourinary Instruments
Foley catheter with inflated balloon
Red Robinson catheter
Coude-tip catheter
12-mL Luer-Lok syringe
Notes: Refer to Table 24.7 in the textbook, as well as Figure 24.22.

## Slide 17: Drapes and Sutures
Disposable surgical drapes are placed over operative area using sterile technique
Ideal suture material is easy to handle and knot, nonallergenic, strong without cutting through tissue, can be sterilized
Notes: The physician will request a certain type of suture based on the specific properties of the suture material, the desirable rate of absorption, the size of the suture, and the type of needle the physician prefers.
Refer to Figures 24.23 and 24.24 in the textbook.

## Slide 18: Types of Suture Materials
Absorbable sutures are dissolved by the body during healing process
  Used for deep incisions or lacerations or when removal is difficult
Nonabsorbable suture material is left until healing is complete in minor procedures
  Surgical staples are made of stainless steel or titanium
Notes: Ideal suture material is easy to handle, makes a secure knot, does not cause a localized tissue reaction, is nonallergenic, has adequate strength without cutting through tissue, and can be sterilized.
What common material is often used for nonabsorbable sutures? (A common, nonabsorbable suture material is silk because it is strong and easy to tie. It is treated with a coating to prevent tissue drag and flaking.)

## Slide 19: Suture Sizing and Packaging
Available in variety of diameters and lengths
Diameter of the suture strand determines its size
  Smaller gauges are numbered 0 (aught)
  Larger gauges are identified with numbers above 0
Length of suture material may vary
  Strands precut in 18-, 24-, 54- and 60-inch lengths

## Slide 20: Needles
Surgical needles are chosen according to the area in which they are to be used and the depth and width of the desired suture
Point of a needle can be a taper or a cutting edge
Notes: Needles are manufactured with the suture material attached, or swaged, to the needle.
Refer to Figure 24.25 in the textbook to see a swaged suture needle.

## Slide 21: Other Closure Materials
Surgical staples applied with specific staple instruments
Steri-Strips: self-adhesive tape placed over wounds
Tissue adhesives (similar to glue)
Notes: Refer to Figures 24.26 through 24.28 in the textbook to see a disposable skin stapler, a surgical staple remover, and a wound closed with Steri-Strips.

## Slide 22: Advantages of Tissue Adhesive
Saves time during wound repair
Creates a flexible, water-resistant protective coating for the wound
Eliminates the need for suture removal
Results in better cosmetic outcomes because there is no scarring from suture entry
May also be used on larger wounds for which subcutaneous sutures are needed
Especially helpful in pediatric patients or individuals afraid of needles

## Slide 23: Surgical Asepsis and Preparation of Surgical Instruments
Asepsis: Condition of being free of infection or infectious material
Medical asepsis: Reduction of microorganisms and the prevention of transfer of microorganisms
Surgical asepsis: Complete destruction of microorganisms
Notes: Surgical asepsis is a mandatory technique for any procedure that invades the body’s skin or tissues, such as surgery.

## Slide 24: Care and Handling of Instruments
Success of procedure depends on quality of instruments
All instruments should be carefully examined when they are purchased
After surgical procedure, contaminated instruments should be placed in basin of disinfectant solution
Instruments should be cleaned while submerged to prevent airborne spread of microorganisms
Mechanical washing can be used for most instruments
Notes: Refer to Figure 24.29 in the textbook to see an ultrasonic cleaner unit.
After sanitization and inspection, the instruments are ready for the sterilization process.

## Slide 25: Sterilization
Cleansing process that removes all organic material and reduces the number of microorganisms to a safe level
Should be completed immediately after instruments are used
Always wear utility gloves
Disinfection: Process of killing pathogenic organisms or rending them inactive
Notes: Before an instrument or piece of equipment can be used in a surgical procedure, it must be sanitized, then disinfected, and finally sterilized to remove all forms of microorganisms.
Refer to Table 24.8 in the textbook to discuss common factors influencing the effectiveness of sterilization.
Many types of disinfecting agents are available, and they have varying degrees of effectiveness.

## Slide 26: Autoclave
Uses moist heat and pressure to achieve sterilization
Pressure allows for heat higher than boiling point
  To be effective, steam moisture must come in contact with all surfaces being sterilized
Recommended temperature is 250º to 255º F
Incorrect operation may result in superheated steam
Notes: Sterilization can be achieved by moist heat, dry heat, ultraviolet or ionizing radiation, or gas, or with chemicals.
Refer to Figure 24.30 (to see a steam autoclave) and Table 24.9 (to discuss tips for improving autoclaving techniques) in the textbook.
The main cause of incomplete sterilization in the autoclave is the presence of residual air.

## Slide 27: Wrapping Materials
Maintaining sterility of autoclaved package depends completely on wrapper and method of wrapping
  Wrapping paper must be permeable to steam but impervious to contaminants
Types of wrapping used for instruments that are to be autoclaved:
  Disposable double-ply autoclave paper
  Peel-apart polypropylene bags
Double-layered autoclave paper provides multiple layers of protection
Notes: Refer to Figure 24.31 in the textbook to see sterilization pouches with sterilization indicators.
A wrapper should not be used if it is torn or has a hole in it.

## Slide 28: Wrapping Instruments
Must allow pack to be opened without becoming contaminated
Discard autoclave paper that is torn or has holes
Wrap all hinged instruments in the open position
Place gauze square around tips of sharp instruments
Notes: If a number of instruments are to be placed on a stainless-steel tray for wrapping, first place a double-folded towel on the tray, and then position the instruments. This helps to protect them.
Polypropylene is a plastic capable of withstanding autoclaving but is resistant to heat transfer.
When using sterilizing bags, insert the handles of the instruments into the end of the bag that will be opened first to ensure that the grasping end of the instruments can be reached easily when the bag is opened.
When using two-ply autoclave paper, use specialized autoclave tape to seal the package.
Label each pack according to the instruments contents and sterilization date and write your initials.

## Slide 29: Sterilization Indicators
Chemical
  Autoclave tape
  Placed inside instrument packages to verify steam and heat penetration of the wrapping
Biologic
  Perform procedure weekly
  Results should be documented
Notes: Refer to Figure 24.32 in the textbook to see autoclave tape.
The healthcare facility should have a policy for how frequently the autoclave is tested using biologic sterilization indicators.

## Slide 30: Quality Assurance Records for Office Sterilization
Every office should have specific protocols
Regular maintenance
Keep a log
File reports as necessary
  Identify nature of problem, how it was corrected, and when
  Date and time
  Subsequent and successful sterilization run

## Slide 31: Loading the Autoclave
Prepare all packs and arrange load in a way that allows maximum circulation of steam and heat
Rest articles on edges; don’t overcrowd
Instruments may be autoclaved unwrapped if they do not need to be sterile when used later
Notes: Refer to Procedure 24.2 in the textbook to discuss how to operate an autoclave.

## Slide 32: Unloading Guidelines
Once pressure gauge reads “0,” stand back from door and open door approximately ¼ inch
  Wear heat-resistant gloves
Allow load to dry for at least 15 minutes
Dry, wrapped packs may be removed with clean, dry hands
Place packs on dry, dust-free surface inside an enclosed cupboard or storage drawer

## Slide 33: Shelf Life of Sterilized Packs
CDC no longer identifies specific time for shelf life of sterilized packs
All sterile packs should be stored on dry, dust-free, covered shelves or in drawers
Quality of packaging material, storage conditions, and how much the packs are handled all affect possibility of contamination
Notes: General recommendation is that as long as the sterilized items are stored so that packaging material remains intact and undamaged, then the pack is considered sterile.
Any package that is wet/turn/dropped/damaged should be sanitized, disinfected, and wrapped in new autoclave paper or placed in new autoclave pouches, and autoclaved again.

## Slide 34: Chemical Sterilization
Used for instruments that cannot be exposed to the high temperatures of steam sterilization
Must avoid skin contact with sterilizing solution
Use of chemicals for sterilization is not very practical in ambulatory facility
Use of liquid chemicals should be restricted
Notes: Sterilizing chemical solution must be mixed correctly exactly according to the instructions on the bottle.

## Slide 35: Legal and Ethical Issues
Know what surgery is planned and whether the patient has been informed about the procedure
Realize the full extent of your role as the patient’s advocate and the physician’s agent
Confirm that the physician has explained the surgery to the patient and that the patient has signed informed consent
Notes: The better the patient’s understanding, the greater the likelihood that he or she will comply with presurgical preparations and postsurgical care.