## Slide 1
Vital Signs
Chapter 20
The next 5 slides are your learning objectives

## Slide 2: Vital Signs
Do the following related to temperature:
  Cite the average body temperature for various age groups.
  Describe emotional and physical factors that can cause body temperature to rise and fall.
  Convert temperature readings between Fahrenheit and Celsius scales.
  Obtain and record an accurate patient temperature using three different types of thermometers.

## Slide 3
Do the following related to pulse:
  Cite the average pulse rate for various age groups.
  Describe pulse rate, volume, and rhythm.
  Locate and record pulse at multiple sites.
Do the following related to respiration:
  Cite the average respiratory rate for various age groups.
  Demonstrate the best way to obtain an accurate respiratory count.
Vital Signs

## Slide 4
Do the following related to blood pressure:
  Cite the approximate blood pressure range for various age groups.
  Specify physiologic factors that affect blood pressure.
  Differentiate between essential and secondary hypertension.
  Interpret current hypertension guidelines and treatment.
  Describe how to determine the correct cuff size for individual patients.
  Identify the different Korotkoff phases.
  Accurately measure and document blood pressure.
Vital Signs

## Slide 5
Discuss and perform pulse oximetry.
Accurately measure and document height and weight, use the body mass index scale, and convert kilograms to pounds and pounds to kilograms.
Vital Signs

## Slide 6: Vital Signs
Four vital signs:
  Temperature
  Pulse
  Respiration
  Blood pressure
Anthropometric measurements
  Usually measured at the same time as vital signs
Notes: These signs are the human body’s indicators of internal homeostasis and the patient’s general state of health.
Because medical assistants are chiefly responsible for obtaining these measurements, it is imperative that they have confidence in the theoretic and practical applications of vital sign measurement.
Though the medical assistant obtains vital signs routinely, it is a task that requires consistent attention to accuracy and detail.
What are the anthropometric measurements? (These measurements include height, weight, body mass index [BMI], and other body measurements, such as fat composition and an infant’s head circumference.)

## Slide 7: Factors that May Influence Vital Signs
Influenced by physical and emotional factors
  Patient may have had a hot or cold beverage
  Patient could be anxious
  Patient could be nervous
  Patient could have elevated heart rate because of racing to get to the appointment
  Patient could be in pain
Medical assistant must help the patient relax before taking any readings
Notes: Measurements sometimes must be obtained a second time, after the patient is more calm or comfortable.

## Slide 8: Temperature
Factors affecting body temperature
  Age
  Stress and physical activity
  Gender
  External factors
Fever
  Continuous
  Intermittent
  Remittent
Notes: Body temperature is defined as the balance between heat lost and heat produced by the body.
The temperature of younger children fluctuates due to external factors, and older individuals lose ability to respond therapeutically to temperature extremes.
The secretion of hormones during the menstrual cycle causes fluctuations in temperature.
Explain the three types of fevers. (Continuous fevers stay above the normal range, but fluctuate 3 degrees or less. Intermittent fevers come and go, alternating between elevated and normal temperatures. Remittent fevers fluctuate considerably and never return to the normal range. Refer to Figure 20.1 in the textbook.)
Patients with fever usually have loss of appetite (anorexia), headache, thirst, flushed face, hot skin, and general malaise.

## Slide 9: Temperature Sites
Axillary
Oral
Tympanic
Rectal
Temporal artery
Notes: Refer to Table 20.1 in the textbook.

## Slide 10: Temperature Readings
Use either Fahrenheit or Celsius scale
Tympanic, digital, or temporal artery (TA) scanner thermometers used
  TA scanner most accurate for infants
Oral temperatures are not accurate for children
  Children are unable to hold thermometer under the tongue
Notes: If the ambulatory care setting where you work uses a Celsius thermometer, patients may ask you what the temperature is in Fahrenheit degrees because that is the scale they understand.
You should write (T) for tympanic, (R) for rectal, (A) for axillary, or (TA) for temporal artery readings after recording the temperature to clarify that an alternative site was used.
For patients younger than 3 years, and for those unable to hold a thermometer properly in their mouth during the procedure, a tympanic or temporal thermometer can be used.

## Slide 11: Converting Temperature Readings
º C = (º F − 32) × 5/9
º F = (º C × 9/5) + 32
Notes: The Fahrenheit scale is used most often in the United States, but hospitals and many ambulatory care settings use the Celsius scale.

## Slide 12: Types of Thermometers and Their Uses
Digital thermometers
  Blue probe: axillary
  Red probe: rectal
Tympanic thermometers
Temporal artery scanner
Notes: A digital thermometer beeps when the process is completed (10 to 60 seconds), and the reading appears on a light-emitting diode (LED) screen on the face of the instrument; there is reduced risk of cross-infection.
Refer to Figure 20.2 to see a digital thermometer and Figure 20.3 to see a tympanic thermometer.
Both the speed and comfort of a tympanic thermometer have greatly influenced its popularity, but it shouldn’t be used if the patient has bilateral otitis externa or if impacted cerumen is present in both ears.
Figure 20.4 shows the temporal artery scanner, which uses an infrared beam to assess the temperature of the blood flowing through the temporal artery of the lateral forehead.
Procedure 20.1 describes how to obtain an oral temperature using a digital thermometer.
Procedure 20.2 describes how to obtain an axillary temperature using a digital thermometer.
Procedure 20.3 describes how to obtain a rectal temperature of an infant using a digital thermometer.
Procedure 20.4 describes how to obtain a temperature using a tympanic thermometer.
Procedure 20.5 describes how to obtain a temperature using a temporal artery thermometer.

## Slide 13: Pulse Sites
Temporal
Carotid
Brachial
Radial
Femoral
Popliteal
Dorsalis pedis
Notes: Figure 20.5 shows pulse sites.
The temporal pulse is located in the temple area of the skull, parallel and lateral to the eyes. Refer to Figure 20.6.
The carotid artery is located between the larynx and the sternocleidomastoid muscle in the front and to the side of the neck and is most frequently is used in emergencies and to check the pulse during CPR. Refer to Figure 20.7.
An apical count may be requested if the patient is taking cardiac drugs or has bradycardia or tachycardia.
To determine the presence of a pulse deficit, the physician may listen to the apical beat while the medical assistant counts the pulse at another site.
The brachial pulse is the artery that is felt and heard when blood pressure is measured. Refer to Figure 20.8.
The radial artery is the most frequently used site for counting the pulse rate, the femoral pulse is located where the femoral artery passes through the groin, and the popliteal pulse requires the patient to be in a recumbent position with the knee slightly flexed.
Procedure 20.6 describes how to obtain an apical pulse.

## Slide 14: Characteristics of a Pulse
Rate
  Heartbeats felt as blood moves through the artery (1 min)
  Lost body heat means increased circulation
Rhythm
  Time between pulse beats
  Arrhythmia
  Intermittent pulse
Volume
  Strength of heart as it contracts
Notes: Because the body must balance heat loss by increasing circulation (a faster heart rate), the pulse rate is proportionate with the size of the heart.
What causes varying pulse rates? (Pulse rates normally vary as a result of a person’s age, body size, gender, and health status.)
An abnormal rhythm, or arrhythmia, is described according to the rhythm pattern detected.
An intermittent pulse may occur in healthy individuals during exercise or after drinking a beverage containing caffeine.

## Slide 15: Approximate Age- Related Pulse Rates
Newborn Range: 120-160 beats/min
  Average: 140
1-2 Years Range: 80-140 beats/min
  Average: 120
3-6 Years Range: 75-120 beats/min
  Average: 100
7-11 Years Range: 75-110 beats/min
  Average: 95
Adolescence to adulthood: 60-100 beats/min
  Average: 80
Notes: Refer to Table 20.2 in the textbook.

## Slide 16: Three-Point Scale for Measuring Pulse Volume
3+: Full, bounding pulse
  Pulsation is very strong and does not disappear with moderate pressure
2+: Normal pulse
  Pulsation is easily felt but disappears with moderate pressure
1+: Weak, thready pulse
  Pulsation is not easily felt and disappears with slight pressure

## Slide 17: Determining the Pulse Rate
Radial and apical
  Have patient in a relaxing position
  Use the correct pressure
Femoral, popliteal, pedal
  Difficult to find and hear
Notes: Figure 20.10 shows a Doppler ultrasound unit used to measure the pedal pulse.
Too much pressure obliterates the patient’s pulse, and too little pressure prevents detection of irregularities or of all the beats.
A Doppler unit, which is an ultrasound unit that magnifies the pulsation, may be used to locate and count these pulses accurately.

## Slide 18: Respiration
Physiology
  Inspiration and expiration
  Internal and external
Characteristics of respiration
Counting respirations
Notes: What is the purpose of respiration? (The purpose of respiration is to provide for the exchange of oxygen and carbon dioxide among the atmosphere, the blood, and the body cells.)
During the inspiratory phase, the diaphragm contracts and drops down, causing the lungs to expand and fill with air. During the expiratory phase, the diaphragm returns to its normal, elevated position, causing the lungs to expel the waste air back into the atmosphere.
Internal respiration occurs at the cellular level, when oxygen in the bloodstream is transferred into the cells for energy and carbon dioxide is released as a waste product and transported back to the lungs for exhalation.

## Slide 19: Characteristics of Respirations
Rate
  Normal, rapid, slow
  Breathing alternations
  Respond to exercise, emotional upsets
Notes: Figure 20.11 shows respiratory rate patterns, called spirograms, which are recorded using a spirometer.
Dyspnea occurs in patients with pneumonia, asthma, or chronic obstructive pulmonary disease (COPD) and after physical exertion or at very high altitudes.
Other alterations in breathing are bradypnea, apnea, tachypnea, and hyperpnea.

## Slide 20: Characteristics of Respirations
Rhythm
  Breathing patterns
Depth
  Amount of air inhaled/exhaled
Notes: What are some things considered normal concerning rhythm? (Automatic interruptions, such as sighing, are considered normal.)
Noticeable breath sounds are a sign of certain diseases, such as pneumonia, asthma, and pulmonary edema.

## Slide 21: Approximate Age-Related Respiration Ranges
Newborn Range: 30-50
  Average: 40
1-3 Year Range: 20-30
  Average: 25
4-6 Year Range: 18-26
  Average: 22
7-11 Year Range: 16-22
  Average: 19
Adolescence to Adulthood Range: 12-20
  Average: 16
Notes: Refer to Table 20.3 in the textbook.

## Slide 22: Counting Respirations
Don’t mention you’re counting them
  Patients self-consciously may alter breathing
Count for 30 seconds; multiply by 2
Record variations on the patient chart
Notes: Keep your eyes alternately on the patient’s chest and your watch while you count the pulse rate, and then, without removing your fingers from the pulse site, determine the respiratory rate.
Do not use the 15-second interval because this count can vary by a factor of +4 or –4, which is significant when dealing with such a small number.
Procedure 20.7 describes how to assess the patient’s radial pulse and respiratory rate.

## Slide 23: Blood Pressure
Factors affecting blood pressure
Evaluating the blood pressure
Measuring blood pressure
Systolic and diastolic measurements
Notes: The systolic pressure is the highest pressure level that occurs when the heart is contracting and the first pulse beat is heard; the diastolic pressure is the lowest pressure level when the heart is relaxed and the last sound is heard.
The difference between systolic and diastolic blood pressures is the pulse pressure.
The blood pressure is recorded as a fraction, with the systolic reading the numerator (top) and the diastolic reading the denominator (bottom).

## Slide 24: Approximate Age-Related Blood Pressure Ranges
Newborn
  Systolic Range, 60-96; Diastolic Range, 30-62
1-3 Years
  Systolic Range, 78-112; Diastolic Range, 48-78
4-6 Years
  Systolic Range, 78-112; Diastolic Range, 50-79
7-11 Years
  Systolic Range, 86-114; Diastolic Range, 52-79
Adolescent
  Systolic Range, 94-119; Diastolic Range, 58-79
Adult
  Systolic Range, 100-119; Diastolic Range, 60-79
Notes: Refer to Table 20.4 in the textbook.

## Slide 25: Factors Affecting Blood Pressure
Blood volume
  Increased or decreased
Peripheral resistance (blood viscosity)
  Blood flow through the lumen
Vessel elasticity
  Artery ability to expand and contract
Condition of heart muscle and arterial walls
  Myocardium is primary determinant
Notes: An increased blood volume raises the blood pressure, and a decreased blood volume lowers the blood pressure.
The peripheral resistance of blood vessels refers to the relationship of the lumen (the diameter of the vessel) to the amount of blood flowing through it. The smaller the lumen, the greater the resistance to blood flow.
With age, lifestyle factors, or the presence of arteriosclerosis, vessel elasticity may decrease, causing the arterial walls to become firm and resistant; as a result, the blood pressure increases.
If the myocardium becomes weak, pressure in the vessels begins to increase in an attempt to maintain an adequate level of circulating blood to meet the oxygen and nutrient needs of the body.

## Slide 26: Evaluating the Blood Pressure
Secondary hypertension
  Caused by an underlying pathologic condition
Essential hypertension
  No single identified cause
  Systolic pressure is 140-159 or higher; diastolic pressure is 90-99 or higher
Notes: Temporary hypertension may occur with stress, pain, exercise, and exhaustion.
Essential hypertension has no single identified cause but is associated with obesity, a high blood level of sodium, elevated cholesterol levels, and family history.
Primary hypertension is diagnosed if the patient’s blood pressure is persistently higher than 119 mm Hg systolic and/or 79 mm Hg diastolic at two or more office visits over several weeks or months.

## Slide 27: Stages of Hypertension
Normal: Less than 120-80 mm Hg
Elevated: Systolic between 120-129 and diastolic less than 80 mm Hg
Stage 1: Systolic between 130-139 or diastolic between 80-89 mm Hg
Stage 2: Systolic at least 140 or diastolic at least 90 mm Hg
Hypertensive crisis: Systolic over 180 and/or diastolic over 120
Notes: Refer to Table 20.5 in the textbook.

## Slide 28: American Heart Association Guidelines
Three stages
  Prehypertension
  Stage I hypertension
  Stage II hypertension
Guidelines
  Lifestyle changes before medical treatment
  Over age 50, treated for systolic >140
  Blood pressure medications
  Patient-centered treatment
Notes: What is the goal of these guidelines? (The goal of the new recommendations is to reduce the number of people who die each year from hypertension-related illnesses such as coronary artery disease, heart attack, heart failure, kidney disease, and stroke.)
Who is at the greatest risk for hypertension? (People of African-American descent, middle-aged and elderly people, patients with diabetes mellitus, and those with kidney disease.)

## Slide 29: Measuring Blood Pressure
Measured with a sphygmomanometer
  Regularly recalibrated
  Checked for accuracy
    Correct when no more than 3 mm Hg
  Must be used with a stethoscope
Blood pressure cuffs
Notes: The needle on the aneroid dial sphygmomanometer should rest within the small square or circle at the bottom of the dial. The dial can be calibrated by connecting it to a calibrated manometer.
If you have patients who are monitoring their pressure at home, be sure that they understand the mechanics of obtaining a reading accurately.
Procedure 20.8 describes how to determine a patient’s blood pressure.

## Slide 30: Blood Pressure Cuff Sizes
Small adult cuff (22-26 cm arm circumference)
  9 inches
Adult cuff (27-34 cm arm circumference)
  Up to 13 inches
Large adult cuff (35-44 cm arm circumference)
  14-17 inches
Adult thigh cuff (45-52 cm circumference)
  18-20 inches
Notes: Refer to Table 20.6 in the textbook.

## Slide 31: Effects of Body Position on Blood Pressure Measurement
Blood pressure usually taken with patient in either sitting or supine position
  Diastolic pressure can be as much as 5 mm Hg higher when patients are sitting than when they are supine
Patients should not cross their legs during reading
Make sure position of arm is correct
  At level of heart; resting

## Slide 32: Common Causes of Errors in Blood Pressure Readings
Limb used for measurement is above the level of heart
Bladder in cuff is not completely deflated before a reading is started/retaken
Pressure of cuff is released too rapidly
Patient is nervous or anxious
Patient drank coffee or smoked cigarettes within 30 minutes of measurement
Cuff was applied improperly
Cuff is too large or not placed around arm smoothly
Notes: Also, the bladder might not be centered over the artery, there could have been a failure to wait 1 to 2 minutes between measurements, or the instruments are defective.

## Slide 33: Korotkoff Sounds
Phase I
  Sound heard as cuff deflates
Phase II
  Produces swishing sound if heard
Phase III
  Sharp, rhythmic tapping
Phase IV
  Soft, muffled tapping
Phase IV
  All sounds disappear
Notes: During phase II, if you do not follow proper procedure in inflating the cuff, you may not hear these sounds because of their soft quality.
If you do not inflate the cuff enough, you will miss the first two phases completely, and you will incorrectly interpret the beginning of phase III as the systolic blood pressure (phase I).
During phase IV, sounds may disappear in children, in patients of any age after exercise or with a fever, or in a pregnant patient with anemia.

## Slide 34: Palpatory Method
Palpate radial pulse
Inflate until pulse disappears; add 30 mm Hg
Don’t remove fingers during this process
Notes: The diastolic and Korotkoff phases cannot be determined by this method.
This method can be very useful in times of a medical emergency, such as shock, when the patient’s blood pressure cannot be auscultated.
See the unnumbered boxed in the textbook for OSHA’s guidelines for measuring vital signs.

## Slide 35: Pulse Oximetry
Noninvasive method of evaluating both pulse rate and oxygen saturation of blood
May also be referred to as saturation of peripheral oxygen
Medical assisting clips a probe on patient’s earlobe or finger
Normal pulse oximetry reading is 95% or higher
Notes: Procedure 20.9 in the textbook describes how to perform pulse oximetry.
Fingernail polish must be removed before the clip is applied. If patient has artificial nails, the earlobe should be used.
Treatment, such as oxygen or bronchodilator therapies, usually is started when readings are 90% to 92% or lower.

## Slide 36: Anthropometric Measurements
Measuring weight and height
  Obtain with accuracy and empathy
  BMI is used to ascertain disease risk
  Keep the scale where privacy is ensured
Notes: If this is the patient’s first visit, anthropometric measurements are written in the history database and are used as reference information during future visits as needed.
What are some diseases that require weight monitoring? (Hormone disorders [e.g., diabetes], growth patterns [seen in children], and eating disorders [e.g., obesity, bulimia] require accurate weight checks as part of every medical visit.)
When patients are unstable, assist them onto the scale and help them balance themselves.
Procedure 20.10 describes how to measure a patient’s weight and height.

## Slide 37: Converting Kilograms to Pounds
1 kg = 2.2 lb
  Multiply the number of kilograms by 2.2
1 lb = 0.45 kg
  Multiply the number of pounds by 0.45, or divide the number of pounds by 2.2 kg
Notes: If the physician prescribes weight measurement at home, make sure the patient understands the importance of weighing himself or herself each day at the same time in clothing of similar weight.

## Slide 38: Patient-Centered Care
Accurate and safe thermometer use
Obtaining pulse
Tracking respirations
Measuring blood pressure
Weight management
Notes: Use diagrams to teach pulse points, and have the patient measure your pulse to assess the patient’s accuracy and to provide any needed assistance.
The patient and all caregivers also should be taught self-assessment of impending complications and how to perform preventive breathing exercises.
Have an assortment of weight management literature available for the patient to take home, and use community resources when indicated to help the patient with weight-related issues.
Keep in mind that results of vital signs can cause patient anxiety and concern.