## Slide 1
Results
Impact of Weather Conditions on 5G Communication Channel
between connected Vehicles
1Dr Esmail Abuhdima, 1Ahmed El Qaouaq, 1 Shakendra Alston
Computer Science Physics and Engineering Department
Benedict College, 1600 Harden Street, Columbia SC
Abstract
Research problem and theory
Results
Conclusion
Acknowledgements
Recent researches focused on ways to improve the Vehicle to Vehicle Communication (V2V), based on the 5G Technology. The V2V application is required because it will reduce the risk of accidents up to 70%-80%, improve the traffic management, reduce congestion, and improve the fuels consumption. The feature of autonomous vehicles applications requires high bandwidth transmission channel, so the 5G communication channel is reliable solution to support this technology. The dedicated short-range communications (DSRC) which is characterized with frequency bandwidth of 5.9 GHz (4G spectrum) was used as a vehicular connectivity with bandwidth up to 200 mb/s and limited capacity. The 5G band can support connected multiple autonomous vehicles with high data rate and large bandwidth. In this research, the 5G communication channel is considered as a vehicular connectivity since it has a very high bandwidth in the millimeter waves spectrum range. The quality of 5G wireless communication channels between connected vehicles is affected by weather conditions such as rain, snow, fog, dust, and sand. The main objective of this research is to study and estimate the effect of the dust and sand on the propagation of millimeter waves. The Mie model is used to investigate the effect of dust and sand storms on the propagating mm-waves. The effect of dust and sand on the communication path loss of DSRC and 5G frequency band is investigated in the case of Urban area and the Highway condition. Results show that, the attenuation of dust and sand is changed when the particle size of sand, frequency of propagating wave, and concentration of dust are changed. Finally, the new model of link margin is created to estimate the effect of dust and sand on DSCR (5.9 GHz) and 5G (28 GHz) communication path loss.
The geometry of research is shown in Fig. 1. In this research, the Mie Model was used to investigate the effect of dust and sands on the propagating mm-waves between connected vehicles. The simulation shows the attenuation of propagating signal is increased when the operating frequency, particle size and concentration of dust are increased as shown in Fig. 2, 3, 4, and 5. The path loss was taken in consideration in the two driving conditions (Urban and Highway).
In this research, the effect of dust and sand on the 5G wireless communication channel between connected vehicles was investigated.
The attenuation of the propagating signal increases when the operating frequency, Concentration of the dust and the particle size of sand are increased.
The 5G mm-wave communication channel is more effected by dust and sand storms than the DSRC channel.
The real measurement of dielectric constant, particle size range and concentration of dust of the desert region in the united state should be considered.
This work was supported by
we acknowledge support from Dr. Comert
The USDOT Center for Connected Multimodal Mobility (Tier1 University Transportation Center) Grant
HBCU-UP Implementation: HRD-1436222, Dr. Raychoudhury
Virtual Summer Research Internship, Dr. Mbamalu
HBCU-UP Implementation Project # HRD-1436222, SURI, Dr. Furrer
Figure 1. Autonomous intersection and weather elements
The link margin is defined by:
+ -10-
The attenuation of dust and sand is defined by
where,
, Receiver front-end noise figure F = 6dB,
= (+ +c3 ) (Attenuation Equation),
c1
++
c3=379
The Path Loss is defined by:
Fig. 2 Attenuation versus the visibility at f)
Fig. 3 Attenuation versus the visibility at f)
Fig. 4 Attenuation versus the particle size at f)
Fig. 5 Attenuation versus the particle size at f)
Scenario | 0% |  | 60% |  | 100% | 
 | 5.9 GHz | 28 GHz | 5.9 GHz | 28 GHz | 5.9 GHz | 28 GHz
Urban | V no effect p.s˃2.6mm | V no effect p.s˃497um | V no effect p.s˃826um | V ˂3m p.S ˃147um | V no effect p.s˃2.6mm | V ˂5m p.S ˃88.7um
Highway | V no effect p.s˃1.77mm | V ˂2m p.s˃130um | V no effect p.s˃432um | V ˂10m p.S ˃21um | V ˂2m p.S ˃55.6um | V ˂2m p.S ˃260um
is the particle size, is the operating frequency and V is the Visibility
ε ′: the dielectric constant , ε ′′: the dielectric loss factor
Scenario | Path loss ()
Urban | 
Highway | 
Scenario | 
Urban | 
Highway |