## Slide 1
Improving Queue Length Estimation Using Particle and Kalman Filters on Low Level Parameters
Dr. Gurcan Comert, Jerodi Hill, Jayla Livingston-Miller
Department of Computer Science, Physics, and Engineering
Benedict College, 1600 Harden St., Columbia, SC 29223
ABSTRACT
With the development of autonomous and connected vehicles, this project develops a reinforcement learning models for estimating queue length at the intersection from these vehicles. This model demonstrates the queue length improvements by develop a system where vehicle to vehicles (v2v) communication and vehicles to infrastructures (v2i) communication would monitor the system. This model also filters the low-level primary parameters (arrival rate and market penetration level) to increase system efficiency of transportation at the intersecting fields. Results provided by VISSIM-microscopic simulation replicates an intersectional scenario like real life by using random seeds. Queue length estimation is one of the inherent key capabilities of connected and autonomous vehicles for operational applications that obtain the information from the connected vehicles from each cycle. These vehicles would commute to the intersectional signal that would translates into information about their location, time, and the number of connected vehicles present for the each of the following queue length. Applying the Kalman Filer benefits this unimodal form by improving the primary parameters to stand in a low level, thus, assuming Poisson distribution with this filter will develop a correlation that would implement a queue length that be coherent in an intersectional scenario.
LAMBDA AND PROBE PROPORTION
From the parameters that communicate from each cycles by the probe vehicles to the traffic signal, it used to assuming the Poisson arrival rate and market penetration level (probe proportion).
POISSON DISTRIBUTION
This study used the Poisson distribution in order to find the queue length estimation. In the graph, it shows different mathematical concept compared to the true queue length. Initially, the rate of Poisson distribution is close to the true queue length. Later, the Poisson distribution follow the true queue length trend The Poisson distribution formula that we are going to use is:
PROBLEM DEFINITION
Queue length estimation (QLE) is one of the inherent key capabilities of connected and autonomous vehicles for operations control. This study aim to estimate the queue lengths without knowing the true parameters as well as the true queue lengths. The problem can summarize as:
  queue lengths show nonlinear behavior with unknown distribution type
  underlying process model is also very complex depending on arrival rate, changing signal timing, day of time, and roadway geometry, etc.
The traffic model on signalized intersections is measured by the queue length which can be used to estimate delays and travel times. Based from a relationship between the incoming vehicles to the traffic signals, the model would be improved from the interaction of the user’s demands of conflict. Analytical closed-form expressions were developed by specific traffic parameter based by a cycle to cycle interaction where the communication from connected and autonomous vehicles and traffic signals share specific data. These parameters are:
In VISSIM, 1000 cycles produced random numbers of probe vehicles that would communicate to the traffic signal. This study aims to formulate and filter the low-level parameters for unimodal distribution case. Using the data, we will formulate a low-level parameters from the traffic parameters from each cycle where we will filter this information to make an estimated queue length that will like the original queue length.
L | : | Location of the last probe vehicle (PV or CAVs or any sampled vehicles) in the order of vehicles from the stop bar from the traffic light
T | : | Time instant of the last PV that joins the book of the queue from the traffic light
M | : | Number of PVs in the queue
R | : | Duration of the signal (Fixed to 45 seconds)
QL | : | The true queue length from each cycle
 | : | Arrival rate in unit vehicle per second (VPS)
P | : | Probe proportion level (0 = p <= 1)
L | : | Location of the last probe vehicle (PV or CAVs or any sampled vehicles) in the order of vehicles from the stop bar from the traffic light
T | : | Time instant of the last PV that joins the book of the queue from the traffic light
M | : | Number of PVs in the queue
R | : | Duration of the signal (Fixed to 45 seconds)
QL | : | The true queue length from each cycle
 | : | Arrival rate in unit vehicle per second (VPS)
P | : | Probe proportion level (0 = p <= 1)
LAMBDA | PROBE PROPORTION
LAMBDA | PROBE PROPORTION
USING THE KALMAN AND PARTICLE FILTERS
Particles in QLE setting has [p, lambda] with weights to each showing how likely they represent true p and lambda values. Initials weights can be uniform.
  (Move) Obtain new information for the cycles as triplets [M, L, T]
  (Update) Update the weights of the particles based on the new estimates from the update’s observations.
  (Resample) Estimate particles that are highly unlikely based on the triplet received and new estimation of parameters. Particles close to the estimates get higher weights.
  (Estimate) Weighted mean and variance of the filtered [p, k].
Kalman Filters are simple and intuitive assuming underlying Gaussian measurements or errors. In our problem, this may not be true. However, it can demonstrate the problem better and easy to implement.
THE RESULTS
Shown above are the results from assuming the Poisson Distribution as it utilize a simple filter for the parameters, lambda and probe proportion. The queue length estimations were formulated based from the combination of each of the formulas for lambda and probe proportion that was filter from a belief of results from 0 to a specific number (0 <= lambda <= 0.272 and 0 <= probe proportion <= 0.5).
ACKNOWLEDGEMENT
HBCU-UP Implementation Project #HRD-1436222.​
U.S. Department of Education Minority Science Improvement Program (MSIEP-Benedict College Creating Achievers in STEM through Academic Support, Mentoring, and research), ​
Center for Connected Multimodal Mobility (C2M2) (USDOT Tier 1 University Transportation Center) Grant headquartered at Clemson University, Clemson, South Carolina, USA. ​
U.S. National Science Foundation (NSF, Nos. 1719501, 1436222, and 1400991) grants. ​
US Dept of Education Minority Science Improvement Program (MSIEP) Benedict College: Creating Achievers in STEM through Academic Support, Mentoring, and Research
REFERENCE
Labbe Jr, Roger R., 2018, Kalman and Bayesian Filters in Python​
(www.kalmanfilter.net), Alex Becker. “Online Kalman Filter Tutorial.” Kalman Filter Tutorial, 2018, www.kalmanfilter.net/kalman1d.html.​
“Figure 2f from: Irimia R, Gottschling M (2016) Taxonomic Revision of Rochefortia Sw. (Ehretiaceae, Boraginales). Biodiversity Data Journal 4: e7720. Https://Doi.org/10.3897/BDJ.4.e7720.” doi:10.3897/bdj.4.e7720.figure2f.
Comert, Gurcan. “Simple Analytical Models for Estimating the Queue Lengths from Probe Vehicles at Traffic Signals.” Transportation Research Part B: Methodological, Pergamon, 3 June 2013, www.sciencedirect.com/science/article/abs/pii/S019126151300074X?via%3Dihub.
Comert, Gurcan. “Queue Length Estimation from Probe Vehicles at Isolated Intersections: Estimators for Primary Parameters.” European Journal of Operational Research, North-Holland, 27 Jan. 2016, www.sciencedirect.com/science/article/abs/pii/S0377221716000850?via%3Dihub.
FUTURE WORKS
Implement more of the Bayes and Kalman Filter in order to have a better connection from the estimated queue length into the true queue length