## Slide 1
Abstract
Research problem and Theory
Simulation Results
Conclusion
Acknowledgements
The behavior of the scattering waves changes according to the object properties which depend on different factors such as shapes and materials of complex objects. With that stated, the scattering of electromagnetic (EM) waves by a translating, electrically conducting cylinder coated with meta-materials will be investigated herein. Metamaterials are a set of artificial materials that have special electromagnetic characteristics. This kind of materials has negative permittivity and negative permeability. Also, Metamaterials are not available or not easily obtainable in nature. The purpose of our research is to create a module that is used to simulate the effect of translating, conducting cylinder coated with meta-materials on scattering waves. The scattering of electromagnetic plane waves by a stationary conducting cylinder coated with meta-materials has been investigated. In this work, The Lorentz transformation is used to analyze the scattering of an incident E-wave by a translating, highly conducting, circular cylinder coated with meta-materials. The MATLAB is used to display the behavior of scattered phase and amplitude in terms of incident E-wave, as well as show how coating the cylinder with metamaterials affects such observations. Results show that the amplitude and phase of scattering field are shifted by the translation of the conducting cylinder. Future work includes extending this analysis to investigate the effect of the movement (Rotation and Translation) of the conducting cylinder coated with meta-materials on the scattered field.
The geometry of research is shown in Fig. 1. In this research, the effect of the translating of the very good conducting cylinder coated with metamaterial on an incident E-wave is investigated.
In this research, the effect of the translation of a very good conducting cylinder coated with meta-materials on the scattering an incident E-wave was investigated.
The effect derived from the translation of the very good conducting cylinder coated with meta-materials showed that there was a shift (Doppler effect).
The backscattered amplitude and phase are shifted to the right when the conducting cylinder moves away from the source.
Similarly, when the conducting cylinder coated with metamaterials moves in the direction of the source, the backscattered phase and magnitude is shifted to the left.
The behavior of the backscattered field of the translating of the very good conducting cylinder coted with meta-materials would be different from the scattered phase and magnitude of the conducting cylinder without meta-materials.
This work will extend to analysis the effect of the movement (Rotation and Translation) of the conducting cylinder coated with meta-materials on the scattered field.
This work was supported by:
U.S. Department of Education Minority Science Improvement Program (MSIEP-Benedict College Creating Achievers in STEM through Academic Support, Mentoring, and Research FY19 US Department of Education MSEIP Grant Award P120A190061)
Center for Connected Multimodal Mobility (C2M2) (USDOT Tier 1 University Transportation Center) Grant headquartered at Clemson University, Clemson, South Carolina, USA.
U.S. National Science Foundation (NSF, Nos. 1719501, 1436222, and 1400991, 1954532) grants.
SC EPSCoR GEAR CRP, SCAMP, NASA ULI project headquartered at University of South Carolina, Columbia.
Figure 1. EM scattering by a cylinder coated with meta-materials.
Components of the scattered field are defined by:
where
The unknown coefficients, and are calculated by using boundary conditions.
Scattering of Electromagnetic Waves from a Translating
Conducting Cylinder Coated with Meta-Materials
Dr Esmail Abuhdima, Tashea Symonette, Conrad Newry, Ibenese Jean-Gilles
Computer Science Physics and Engineering Department
Benedict College, 1600 Harden Street, Columbia SC
Fig. 2. Magnitude of the backscattered electric field at
Fig. 3. Phase of the backscattered electric field at
Fig. 4. Magnitude of the backscattered electric field at
Fig. 5. Phase of the backscattered electric field at
The following approximation to Lorentz transformation is applied to the expression of scattered field
and