## Slide 1: Boosting Lithium-Ion Battery using Silicon-Based Nanomaterials
Introduction
Procedures
Seven methods used to prepare Si nanomaterials were studied to see which would be best to use LiB anode. Two methods that showed great promise are:
Lissan Francis, Krysanna Fuller & Dr. Changyong Qin, Department of Chemistry, Benedict College
1600 Harden St, Columbia, SC 29204
Figure 1. Li-ion Battery System
Results and Discussions
LiB has been portrayed to be an ideal power source for electrical vehicles that will take over traditional engine cars in the near future.
Current LiBs only reach its 1/20 of full potential capacity and face safety issues.
Has low specific capacity of ~200-400 mA.h/g due to poor performance of the anode material.
Si has been proposed as a suitable anode due to its high specific capacity of approximately 4200mA.h/g.
Si materials has ~400% volume expansion during the charge and discharge process which lead to many challenges in the real devices.
Conclusion and Future Work
It was found that the nano Si composites from several of the procedures studied can increase the capacity to about 1000-2000 mA.h/g, which is about 3-6 times that of the LIB with graphene anode. Five of these methods have the following results, a high-capacity of 1056 mA h/g after 800 cycles at a current density of 2000 mA/g, another showed 1000 mA h g−1 at 1 A/g after 100 cycles and high initial CE of 72.9%, another being able to undergo 700 cycles, high areal capacity of 3.29 mA h cm-2 and a high volumetric capacity of 3290 A h cm-3 at 0.09 mA cm-2 and lastly, >92% capacity retention over 500 cycles. All these results proves that the use of Si anode can power electrical vehicles for 500-1000 miles. This result is encouraging and promising for commercialization. The next step is to refine the structure of the nanomaterials as well as to improve the electrolyte so the Si-based LiBs can be safe and efficient in electrical vehicles.
Procedure | Results
Nanopore-embedded graphitic carbon shell on silicon anode | Delivers a high capacity of 1056 mA h g-1 after 800 cycles at a high current density of 2000 mA/g.
Internal and External Design For High Stability Si Nanoparticles | high areal capacity of 3.29 mA h cm-2 and a high volumetric capacity of 3290 A h cm-3 at 0.09 mA cm-2
The nanopore-embedded graphitic carbon shell on Si anode method where Si NP were encapsulated with nano-porous N-doped graphitic carbon through Fe3+-mediated polymerization of dopamine, followed by subsequent carbonization and acid treatment and their performance as an anode for LiBs was investigated.
Acknowledgements
Dr. Changyong Qin, Benedict College
Department of Defense
National Science Foundation
References
Han, B., Liao, C., Dogan, F., Trask, S. E., Lapidus, S. H., Vaughey, J. T., & Key, B. (2019). Using Mixed Salt Electrolytes to Stabilize Silicon Anodes for Lithium-Ion Batteries via in Situ Formation of Li–M–Si Ternaries (M = Mg, Zn, Al, Ca). ACS Applied Materials & Interfaces, 11(33), 29780–29790. https://doi.org/10.1021/acsami.9b07270
Jia, H., Li, X., Song, J., Zhang, X., Luo, L., He, Y., Li, B., Cai, Y., Hu, S., Xiao, X., Wang, C., Rosso, K. M., Yi, R., Patel, R., & Zhang, J.-G. (2020). Hierarchical porous silicon structures with extraordinary mechanical strength as high-performance lithium-ion battery anodes. Nature Communications, 11(1). https://doi.org/10.1038/s41467-020-15217-9
Jung, C.-H., Choi, J., Kim, W.-S., & Hong, S.-H. (2018). A nanopore-embedded graphitic carbon shell on silicon anode for high performance lithium ion batteries. Journal of Materials Chemistry A, 6(17), 8013–8020. https://doi.org/10.1039/c8ta01471j
Phadatare, M., Patil, R., Blomquist, N., Forsberg, S., Örtegren, J., Hummelgård, M., Meshram, J., Hernández, G., Brandell, D., Leifer, K., Sathyanath, S. K., & Olin, H. (2019). Silicon-Nanographite Aerogel-Based Anodes for High Performance Lithium Ion Batteries. Scientific Reports, 9(1). https://doi.org/10.1038/s41598-019-51087-y
The internal and external design for high stability Si NP where the Si NP were treated with acid to form hydroxylated silicon nanoparticle. A conductive polymer was made and used as a coating for the hydroxylated Si NP to form the internal structure. These were then uniformly encapsulated in the small “cells” formed by cross-linked reduced Graphene Oxide (rGO) sheets to form the external structure. Tests such as peeling, conductivity and cycling performance tests were done to test the material characterization of the electrode.
Qi, S., Zhang, X., Lv, W., Zhang, Y., Kong, D., Huang, Z., & Yang, Q.-H. (2019). Electrode Design from “Internal” to “External” for High Stability Silicon Anodes in Lithium-Ion Batteries. ACS Applied Materials & Interfaces, 11(15), 14142–14149. https://doi.org/10.1021/acsami.9b02206
Qi, W., Shapter, J. G., Wu, Q., Yin, T., Gao, G., & Cui, D. (2017). Nanostructured anode materials for lithium-ion batteries: principle, recent progress and future perspectives. Journal of Materials Chemistry A, 5(37), 19521–19540. https://doi.org/10.1039/c7ta05283a
Raić, M., Mikac, L., Marić, I., Štefanić, G., Škrabić, M., Gotić, M., & Ivanda, M. (2020). Nanostructured Silicon as Potential Anode Material for Li-Ion Batteries. Molecules (Basel, Switzerland), 25(4), 891. https://doi.org/10.3390/molecules25040891
Wang, F., Zhao, B., Zi, W. et al. Ionothermal Synthesis of Crystalline Nanoporous Silicon and Its Use as Anode Materials in Lithium-Ion Batteries. Nanoscale Res Lett 14, 196 (2019). https://doi.org/10.1186/s11671-019-3024-9