## Slide 1: Road Surface Distress Detection Using Cell Phone Motion Sensors
In this summer research, we were able to show higher correlations between the same road distress types, i.e., spall, alligator crack, bump. The method uses a rolling horizon framework and moves the mask of a given distress type over time series of sensor data, z-axis acceleration values. With this approach, we can detect multiple distress types with very low computational costs.
As a future study, we plan to fuse this method with deep learning methods to improve overall classification accuracy.
. DL Training (2-3
Major road surface distresses, if not maintained, can cause serious incidents for the users.
Typical maintenance is done over a fixed schedule, after detection with a monitoring vehicle, and based on complaints.
Thus, less expensive and short-term monitoring is needed.
The research goal is to develop a cost-effective approach to monitor the road conditions by cloud-based collaborative monitoring using in-vehicle smartphones from any general public vehicle users.
Using collected and annotated smartphone motion data, the study aims to classify road distresses.
Overall, the study serves as a cloud-based collaborative monitoring approach to fuse all smartphone data to achieve holistic, accurate and complete monitoring.
Antoine Bowleg, Michael Tadese, Gurcan Comet, Negash Begashaw, Computer Science, Physics, and Engineering Department, Benedict College
Akshatha Ramesh, Dhananjay Nikam, Yunyi Jia, Clemson University, C2M2
Spearman Correlation:di:difference between ranks, n: number of observations
Pearson Correlation series of data (x,y):
Figure. Performance of detection using masking and correlations (Spearman)
Figure. Road surface distress types considered and an example mask (https://www.pavemanpro.com/article/identifying_asphalt_pavement_defects/)
U.S. Department of Education Minority Science Improvement Program (MSIEP-Benedict College Creating Achievers in STEM through Academic Support, Mentoring, and Research FY19 US Department of Education MSEIP Grant Award P120A190061)​
Center for Connected Multimodal Mobility (C2M2) (USDOT Tier 1 University Transportation Center) Grant headquartered at Clemson University, Clemson, South Carolina, USA.
U.S. National Science Foundation (NSF, Nos. 1719501, 1436222, and 1400991, 1954532) grants.
SC EPSCoR GEAR CRP, SCAMP, NASA ULI project headquartered at University of South Carolina, Columbia.
Higher correlations between the same road distress types, i.e., spall, alligator crack, bump.
The method uses a rolling horizon framework and moves the mask of a given distress type over time series of sensor data, z-axis acceleration values.
With this approach, we can detect multiple distress types with very low computational costs.
As a future study, we plan to fuse this method with deep learning methods to improve overall classification accuracy.
Bump
Fatigue
Pothole
Spall
Alligator Crack
Fault
Construction Joint