## Slide 2: Testing for Water Quality
Natural Resources and Ecology
Unit 3 – Lesson 3.2 Water Function

## Slide 3: Water Quality
The condition of the body of water or water resource in relation to its designated uses.
  Expressed in terms of the measured value(s) of one or more of indicators in relation to their accepted or implied limits.

## Slide 4: Quality Indicators or Factors
Temperature
pH
Dissolved Oxygen
Biochemical Oxygen Demand
Fecal Coliform
Turbidity
Total Solids
Phosphates
Nitrate
The results of these nine water quality tests are used to calculate the Water Quality Index

## Slide 5: What is the Water Quality Index?
A defined set of water quality indicator results producing a score describing general water quality.
Also known as WQI
Water Quality Index Ratings | 
Excellent | 90 - 100
Good | 70 - 90
Medium + | 50 - 70
Poor | 25 - 50
Very Poor | 0 - 25

## Slide 6: Sources, Sinks and Effects
Sinks
leave the ecosystem
Sources enter the Ecosystem
Effects
The results of too much or too little of a water quality factor

## Slide 7: Temperature
A measure of the thermal energy
of the water molecules.

## Slide 8: Temperature
Shade
Loss at night
Cool inflow
Sunlight
Low flow
Wastewater
Reduced dissolved oxygen
Increased plant growth

## Slide 9: pH
A measure of the concentration of H+ ions in water. An indication of the acidity.
Low pH values indicate high acidity
High pH values indicate low acidity
Environmental Protection Agency. (n.d.). The pH Scale Retrieved from: http://www.epa.gov/acidrain/measure/ph.html.

## Slide 10: pH
CO2
Fertilizer
Acid Rain
Soil Runoff
Fertilizer
Urban Runoff
  Algal blooms
  Mosses
  Fish lose slim coat

## Slide 11: Dissolved Oxygen (DO)
A measure of the amount of oxygen gas dissolved in water.

## Slide 12: Dissolved Oxygen (DO)
Respiration
Decay
Sewage
Atmosphere
Water mixing
Photosynthesis
  Fish and insect death
  Anaerobic decay
  Toxic gases

## Slide 13: Biochemical Oxygen Demand
A measure of the oxygen used by biological and chemical processes in water

## Slide 14: Biochemical Oxygen Demand
Settling
Add oxygen
Sunlight
      Sewage
      City runoff
      Farm runoff
  Fish and insect death
  Anaerobic decay
  Toxic gases

## Slide 15: Fecal Coliform
A measure of the concentration of fecal coliform bacteria in water and used to determine the likelihood of contamination by disease causing organisms.

## Slide 16: Fecal Coliform
Dilution Disinfection
Decomposition
      Sewage
      Livestock
      Wild game
  Rashes, Infections
  Diarrhea, Dysentery
  Hepatitis, Giardia

## Slide 17: Turbidity
A measure of water clarity
Source: United State Geological Survey. 2014. Turbidity. Retrieved from: http://water.usgs.gov/edu/turbidity.html
Notes: Water that is highly turbid is detrimental to an aquatic ecosystem. However, slightly turbid water can be healthy, while clear water may have other pollutants causing it to be unhealthy.

## Slide 18: Turbidity
Settling
Dilution
      Erosion
      City Runoff
      Farm Runoff
  Lower Clarity
  Less Photosynthesis
Higher Temperature

## Slide 19: Total Solids (TS)
Measure of all suspended and dissolved solids in a sample of water

## Slide 20: Total Solids
Settling
Dilution
Decomposition
      Erosion
      City Runoff
      Farm Runoff
  Lower Clarity
  Less Photosynthesis
  Dehydration of animals

## Slide 21: Phosphates
A measurement of the concentration of phosphorus containing compounds in water.

## Slide 22: Phosphates
Plant uptake
Animal uptake
Precipitation
      Human Waste
      Farm Runoff
      Soil Exposure
  Eutrophication
  Increased BOD
  Algal Blooms

## Slide 23: Nitrates
A measurement of the amount of nitrate containing compounds in water
Source: Executive Office of Energy and Environmental Affairs. 2014. Concentrated Animal Feeding Operations (CAFOs) Overview. Retrieved from:
  http://www.mass.gov/eea/agencies/agr/about/divisions/concentrated-animal-feeding-ops-overview-generic.html

## Slide 24: Nitrates
Plant uptake
Soil Uptake
Dilution
      Feedlots
      City wastewater
      Auto emissions
  Eutrophication
  Increased BOD
  Algal Blooms

## Slide 25: References
Johnson, R.L., Holmquist, D.D., & Redding, K. (2007). Water quality with Vernier. Beaverton, OR: Vernier Software and Technology.
Lal, H. (2011). The introduction to the Water Quality Index. Retrieved from http://www.waterefficiency.net/WE/Articles/The_Introduction_to_the_Water_Quality_Index_15374.aspx