## Slide 2: Lumber Calculations
Natural Resources and Ecology
Unit 7 – Lesson 7.2 Timber!

## Slide 3: Value of Forests
“The days have ended when the forest may be viewed only as trees and trees viewed only as timber. The soil and the water, the grasses and the shrubs, the fish and the wildlife, and the beauty of the forest must become integral parts of the resource manager's thinking and actions.”
~Senator Hubert Humphrey, 1976

## Slide 4: Forests
Development of forested areas poses an increasing threat to maintaining the integrity of valuable forest lands.
Intact forest lands supply timber products, wildlife habitat, soil and watershed protection, aesthetics and recreational opportunities.
Notes: The Forest Legacy Program (FLP) is a United States program that supports state efforts to protect environmentally-sensitive forestlands.
The National Conservatory has multiple programs to aid over 30 countries around the world in their efforts to sustain the forests.
Source: http://forestry.ky.gov/Kentuckysstateforests/Pages/ForestLegacyProgram.aspx

## Slide 5: What is the value of a tree?
  Beauty to streets, city parks, yards
  Cleans the air
  Lowers energy costs
  Increases property values
  Improves water quality
  Reduces soil erosion
  Improves storm water control
  Wood, fuel and fiber and habitat
Notes: Some would say the value of a tree is priceless in that a tree brings beauty to a street, city park, or backyard.
The USDA Forest Service Pacific Southwest Research Station's (PSW) scientists in 2011 found that for every $1 spent on planting and caring for a tree, the benefits that it provides are two to five times that investment. Trees provide benefits that also include cleaner air, lower energy costs, increased property values, and improved water quality and storm water control.

## Slide 6: How much wood is in the forest?
Foresters inventory the trees in a forest and calculate the amount of useable wood for lumber. This is called timber cruising.

## Slide 7: Timber Volume Cruise
Measures the volume of useable wood in the forest.
The volume of wood is measured in a unit called ‘board feet’.
Board feet can be determined from the length, width and thickness of a piece of wood.
Notes: Foresters that manage areas for lumber production often conduct volume cruises through a forest. At each sample point of a volume cruise, the forester makes only two measurements per tree.

## Slide 8: Board Feet
Board feet is defined as
  The amount of wood in a piece measuring 12 inches square and one inch thick; a board-foot equals 1″ x 12″ x 12″ = 144 cubic inches.
  A board-foot is a unit of measure common to the United States.
Photo courtesy of http://www.fotosearch.com/photos-images/lumber.html
Notes: A volume table is used with the known diameter and log height of a tree to reveal the volume of wood contained in trees of different diameters and log lengths. More information on using a volume table is given on the slide for Doyle or Scribner Scale.
The use of board feet is used to determine tree measurement for landowners who want to learn more about the value of their timber.

## Slide 9: Calculating Board Feet
For example, a 2″ x 4″ that is 8 feet long has
Or
Notes: Use this method to calculate the number of board feet in lumber of any size after the lumber has been sawed at a mill.
The second method removes the units and ends in board feet unit.

## Slide 10: Volume of standing trees
Determining the volume of standing trees is more difficult than boards. The trees are irregularly shaped, and too tall to climb.
The volume is measured using three tools:
Diameter tape
Biltmore Stick
Doyle Scale
Photo courtesy of http://www.fotosearch.com/photos-images/lumber.html

## Slide 11: Diameter Tape
A form of dendrometer that consists of a cloth or metal tape calibrated in units of pi (i.e., 3.14) that is mainly used to measure diameter at breast height (DBH).
The tape is actually measuring the tree's circumference, but since circumference and diameter are related by pi, the diameter can easily be obtained.
Resulting measurement is an approximation.
Notes: A diameter tape (D-tape) is a form of dendrometer (i.e., study of tree measurements) that consists of a cloth or metal tape that is mainly used to measure diameter at breast height (DBH).
DBH is measured at a fixed height of 4.5 feet (140 cm) above the ground, where it is most convenient to measure diameter.
Diameter is easily measured because the tape is calibrated in units of 3.14 (pi) inches or centimeters.
The tape is actually measuring the tree's circumference but since circumference and diameter are related by pi, the diameter can easily be obtained.
The only problem with the diameter tape is that the measurements assume the tree's trunk cross-sections are perfectly circular. Thus, the diameter tape just gives an approximation; regardless it is the most commonly used dendrometer for DBH.

## Slide 12: Biltmore Stick
One of the basic tools for estimating the height and diameter of standing trees
Called a Biltmore stick, scale stick, or a cruiser’s stick
Converts height in feet to the equivalent number of 16 foot logs
Photo Courtesy of
http://www.dnr.sc.gov/education/Envirothon/pdf/Forestry2014/Makingusingyourowncrusierstick.pdf

## Slide 13: Merchantable Height
The length of usable tree and is measured from stump height, 1 foot above ground to a cutoff height in the top of the tree.
The cutoff height will vary with markets, with the product being produced, and with the presence of excessive limbs.
Factors that make a log unusable for lumber or veneer
  Small diameter-(under 10 inch inside bark)
  Defect occurring on the trunk
Notes: Different than total height, merchantable implies the ability to cut lumber, veneer, or other products from the logs contained in a tree.
There are numerous factors that make a log unusable for lumber or veneer, such as too small diameter (under 10 inches inside the bark) and defects or insect damage.
Merchantable height is controlled by a diameter limit in the upper part of a tree or by some defect occurring on the trunk, such as a fork in the trunk, defect, or smaller limbs, which renders the wood above unsuitable for conversion to products.

## Slide 14: Measuring DBH and number of logs
Measure the DBH using the diameter tape.
Stand 66 feet from the tree being measured.
Using the MERRITT HYPSOMETER side of the Biltmore stick, hold it 25 inches from the eye in a vertical position.
Tilt the head back slightly so that the body does not have to move or the head doesn’t move when reading from stump point to cutoff height.
Read the number of merchantable logs from the from the stump height to the cutoff height.
Do not move the stick while measuring.
Notes: The Biltmore stick has been calibrated so that if you stand 66 feet from the tree being measured and hold the stick 25 inches from your eye in a vertical position, you can read the number of merchantable logs from the stick using the Merritt Hypsometer side of the stick. The line of sight crosses the stick at a number on the Merritt Hypsometer scale indicating the quantity of 16 foot logs that may be cut from the tree. If necessary, for very tall tress walk an additional 33 feet away from the tree.
It is important not to move the stick when taking a measurement; tilt your head back slightly so that you do not have to move your head when reading from stump point to cutoff height

## Slide 15: Doyle Scale
Uses the DBH and number of logs to estimate board feet.
Smaller logs cost more to handle, so the Doyle Scale underestimates the log volume to automatically cover the extra handling cost .
Notes: Doyle Scale estimates the lumber you can get from a log. For smaller logs it under-estimates the actual volume. Smaller logs cost more to handle, so rather than subtract from the actual footage (e.g., using the International 1/4 inch scale), and possibly make the logger upset or pay less for smaller logs, the Doyle scale automatically covers the extra handling cost.

## Slide 16: Board Feet with the Doyle Scale
Use the diameter tape to measure the DBH.
Locate that DBH row on the left vertical axis.
Use Biltmore stick reading for the number of 16 foot logs.
Move along top horizontal axis to the column with that number of logs.
The intersection of the row and column lists the board feet for that tree.
Deductions are made for defects, such as rot and curved trees.
Notes: To use the scale, first measure the average diameter of the small end of the log inside the bark in inches.
Locate that row on the scale.
Next, measure the length of the log in feet.
Move over on the scale to that length column.
Where the two measurements intersect, the result is the board footage for that log.
The process must be repeated for each log.
Deductions are made for defects, such as rot and curved logs.

## Slide 17: References
Illinois Forest Management. (1997). How to measure trees to determine their board-foot volume and value. Vol. 1, 1997, no. 32. Urbana-Champagne, IL: University of Illinois Urbana-Champagne, Cooperative Extension Service.
KY Department for Natural Resources. (2011). Forest legacy program. Retrieved from http://forestry.ky.gov/Kentuckysstateforests/Pages/ForestLegacyProgram.aspx
Bardon, R. E. (n.d.). Woodland owner notes: Estimating the volume of a standing tree using a scale (Biltmore) stick. Raleigh, NC: North Carolina Cooperative Extension Service.
USDA Forest Service. (n.d.). Calculating board footage. Retrieved from http://www.na.fs.fed.us/spfo/pubs/uf/lab_exercises/calc_board_footage.htm