## Slide 2: Sterile Technique for Plant Cloning
Animal and Plant Biotechnology
Unit 4 – Lesson 4.2 Performance Enhanced Plants

## Slide 3: Sterile Technique
Notes: A transfer chamber, laminar flow hood, or bacterial safety cabinet is used to minimize the potential of contaminates being introduced into the culturing dishes.

## Slide 4: Microbial Growth
Agar is rich with nutrients and provides the optimal environment for cell growth.
Growth can be both the intended plant cells and unintended organisms such as bacteria and fungi.
Todar (2006)
Notes: Nutrient rich agar is necessary to support cell growth for tissue culture. However, the conditions are perfect to support the growth of bacteria and fungi. Bacteria has contaminated this culture dish.
Picture is from:
Written and edited by Kenneth Todar University of Wisconsin-Madison Department of Bacteriology All rights reserved
http://www.textbookofbacteriology.net/control.html

## Slide 5: Harmful Organisms
Chang & Chang (1998)
If contaminated, tissue culture environments support harmful bacteria and fungi that may feed on young tender plant tissue.
These organisms may also be harmful to humans – never open a contaminated culture dish.
Notes: Contaminates can feed on tender plant cells and ultimately kill the culture. Other harmful effects can be from bacteria that is harmful to humans. Harmful bacteria, such as strep, can rapidly multiply in the environment meant for plant cell growth.

## Slide 6: Contamination
Bacteria and fungal spores are everywhere; in the air and all over our bodies and room surfaces.
To minimize contamination, all transfer activity should be conducted in a sterile, draft-free chamber.
Notes: Although surfaces appear clean, contaminates are everywhere on every surface. Bacteria and fungal spores can persist in the air and even the plant tissue intended to be cultured. The goal of sterilization is to destroy all contaminates. This is very difficult to accomplish, and at best we can hope to minimize the risk.
The best way to serialize is to use intense heat or pressure (autoclave). Unfortunately, intense heat and pressure would destroy the living plant tissue intended to culture. Sterilization for tissue culture is primarily done by the use of alcohol based chemicals.

## Slide 7: Contamination Prevention
Clean room surfaces prior to starting tissue culture activities. This includes washing down surfaces with disinfectants and sweeping floors.
Eliminate all drafts from doors, windows, and air ducts.
Clean plant tissue with soap and water before working on it.
Notes: Students should be aware that clean conditions are important. If potential contamination risks are eliminated the risk to culture contamination is minimized.

## Slide 8: Sterile Workspace
Spray all surfaces (including gloves) with 70% Isopropanol.
Be sure all instruments and supplies are inside transfer chamber before sterilizing.
Use sterile culture dishes to prepare tissue samples to prevent direct contact with surfaces.
Notes: Three basic rules to keep a sterile workspace.

## Slide 9: Personal Practices
Tie back long hair
Wash hands – wear gloves covering hands and forearms
Move slowly both around chambers and inside chambers
Do not pass objects over sterile medium when transferring
Do not have more items than needed inside transfer chamber
Limit talking
Notes: Continuation of techniques to minimize contamination.

## Slide 10: Sharing Transfer Chambers
When you leave:
Remove culture dishes from chamber once you are finished.
Leave all instruments soaking in isopropanol solution when not in use.
When you go back in:
Apply isopropanol to gloves as you insert arms into chamber.
Must re-sanitize work area by applying a light spray of isopropanol to surfaces.
Notes: More recommendations related to reducing the risk.

## Slide 11: Detecting Problems
Check culture dishes every three days for evidence of microbial growth
  Slimy areas on agar = bacterial growth
  Fuzzy areas on agar = fungal growth
Report to teacher immediately – DO NOT OPEN CULTURE DISHES
Notes: Stress the safety concerns with contaminated cultures. Contaminated cultures must be removed from the growth chamber immediately and placed in an autoclave to destroy organisms.

## Slide 12: References
Carolina Biological Supply Company. (2004). Plant tissue culture: Definitions and techniques [Brochure]. Burlington, NC: Author.
Chang, C., & Chang, W. C. (1998). Regenerating Calli from root explants of Cymbidium ensifolium. Plant Cell Reports, 17, 251-255.
Parker, R. (2004). Introduction to plant science (Rev. ed.). Clifton Park, NY: Delmar.