## Slide 2: Measurement Tools
Agricultural Power and Technology
Unit 2 – Lesson 2.3 Tools of Measurement

## Slide 3: Parts of a Combination Square
Leveling Vile
Metal Rule
Head
Thumbscrew
Notes: The thumb screw is loosened to slide the head of the square along the metal rule called the blade. The leveling vile can be used to determine if a board is straight or level.

## Slide 4: Combination Square
12″ metal rule that has an accuracy of 1/8″ - 1/16″.
Sliding head can be locked along the rule with thumb screw.
Used to lay out 90° and 45° angles.
Used as a marking gauge by holding the head flush against material.
45° angle
90° angle
Notes: A combination square has a metal rule that can measure objects up to 12″ in length. The head can be slid along the metal rule to set specific lengths for marking materials. The head of the square is held flush against the material to mark a 90 degree or 45 degree line.

## Slide 5: Caliper
Measure the inside or outside dimensions of an object between the jaws.
Has a stem to measure the depth of an object.
Used when a high degree of accuracy is needed.
English or metric units.
  Nearest 1/100″ or 1/1000″
  Nearest 1/100mm
Notes: Calipers are highly accurate tools used where precise measurements are needed.

## Slide 6: Types of Calipers
Digital Caliper
Dial Caliper
Zero button
Dial
Notes: Calipers present the measurements in multiple forms that are read differently. A digital provides a numerical decimal reading. A dial caliper has to be read on the dial scale to calculate the correct measurement. Digital calipers are calibrated by pressing the zero button when the jaws are closed. Calibrate the dial calipers by moving the dial to so the zero mark is aligned with the needle when the jaws are closed.

## Slide 7: Parts of a Caliper
Inner dimension Jaws
Outer dimension jaws
Lock
Guide
Stem to measure depths
Scale
Bar
Notes: To use the caliper, it must first be calibrated so the reading is 0.000” when the jaws are together. After it has been calibrated open the jaws and adjust the jaws by pushing the guide with your thumb. Gently place the jaws against the inside or outside of the object and lock the location of by tightening the lock. The digital reading is then read on the caliper.

## Slide 8: Jaw Placement
Outer Dimension
Inner Dimension
Notes: The material being measured should be gently touching the material between the jaws. The jaws should not be compressing the material. Compressing the material can damage the jaws and decrease the accuracy of the measurement.

## Slide 9: Reading a Dial Caliper
Calibrate the caliper by turning the dial so the needle is aligned with the zero on the gauge when the jaws are closed.
Incorrect
Correct
Notes: Use your thumb to turn the dial while the jaws are closed so the needle is aligned with the zero mark on the gauge.

## Slide 10: Reading a Dial Caliper
Read the total number of inches and tenths visible using the scale on the bar.
Read the hundredths and thousandths of an inch on the dial.
Add the total together
  1.1 inch + 0.0.45 inch
  1.145 inches.
1.1″
0.045″
Notes: Read the dial caliper by finding the largest whole inch exposed on the bar of the caliper and adding it to the decimal inches shown on the dial.

## Slide 11: References
Herren, R. (2006). Agricultural mechanics fundamentals and applications. (5th ed.). Clifton Park, NY: Thomson Delmar Learning.
Ryan, V. (2009). The digital caliper. Retrieved from http://www.technologystudent.com/e quip1/vernier1.htm