## Slide 2: Survey Says
Agricultural Power and Technology
Unit 3 – Lesson 3.4 Material Management

## Slide 3: What is Surveying?
Find distances and change in elevations between locations.
  Elevation – vertical difference in height between two points.
Calculate grade of land when elevation of two points is known.
  Grade – slope between two known points of elevation.
Notes: Surveying is used to calculate elevation and grade. An elevation is the vertical height above or below a fixed reference point. A difference in elevation on a land formation will affect the structural soundness of buildings, roadways, and earthen structures.
The grade of land is determined by calculating the slope between known points of elevation. Changing the grade of land can control the flow of water and erosion of the soil.
Surveyors use precise tools and detailed calculations to measure straight lines, distances, elevations, and grade. Surveying requires the work of a team of tradesman and professionals.

## Slide 4: Surveying Tools
Builder’s level
  Makes a 360 degree horizontal plane.
  Tripod
    Holds a builder’s level.
  Leveling rod
  Used to find vertical distances
  Engineer’s and architect’s rod
Notes: Surveyors have three major pieces of equipment they use. A survey team consists of two and uses a tripod, builder’s level, and leveling rod to measure land elevations.

## Slide 5: Setting a Tripod
Find level location.
Set tripod securely in ground with legs 3-4 feet apart.
Press points of tripod firmly into ground.
Align head of tripod with a level line in distance such as a roofline.
Notes: Be sure the tripod is securely set in the ground and fairly level before you attach the builder’s level. The type of surface the tripod is being set on will determine how it will be securely placed.
Attach the surveying instrument securely to a fixed base on a tripod to provide a level plane once the tripod is in place. The builder’s level or transit is attached to a tripod and leveled using adjusting screws.

## Slide 6: Setting a Tripod
Adjust tripod legs to level head of tripod.
Tighten adjustment screws legs.
Notes: Adjust tripod legs by releasing locking levers to level head of tripod. Tighten adjustment screws on the legs so tripod will not move when attaching builder’s level

## Slide 7: Builder’s Level
Telescoping device
Attached to the tripod.
Protect lens until level is securely in place.
Adjusting screws level the instrument.
Focus adjustment used to view rod.
Notes: A builder’s level is an instrument used to determine elevations between two specific points. The level has a telescoping device attached to a circular base with adjusting screws. The level is very sensitive and can be broken, easily. Handle with care.

## Slide 8: Leveling a Builder’s Level
Turn telescope parallel to two leveling screws.
Center bubble on the instrument by turning screws at same time.
  Inward moves bubble to right.
  Outward moves bubble to left.
Notes: Use the screws to raise and lower the instrument to make a level line of site. The line of site is a horizontal line that does not curve or bend. This line can rotate along a 360 degree horizontal plane and remain level the entire time.

## Slide 9: Leveling a Builder’s Level
Rotate telescope 90 degrees over third screw.
Adjust screw until bubble is in center.
Rotate level over each screw.
Bubble should remain in the center.
Notes: Rotate the level 360 degrees after leveling. If the bubble does not move, it is level. Repeat the leveling process if the bubble does move.

## Slide 10: Reading a Rod
Rod held vertically to the ground.
Numbers are read from the ground up.
Rod reader will read measurement using builder’s level.
Notes: To use a reading rod, one person needs to hold the rod vertical to the horizontal plane and another must read the rod by looking through the telescope of the leveling instrument. The numbers are read from the ground up. The closest red number below the crosshair seen in the builder’s level telescope is the number of feet. The closest black number below the crosshairs is the number of inches or tenths of a foot.

## Slide 11: Architect’s Rod
Measures in feet and inches.
Red numbers show number of feet
Black numbers show number of inches
Top and bottom of each line represents 1/8 of an inch.
Notes: The architect scale will show the number of feet in red with graduated marks. The black numbers represent the number of inches. Small black graduated marks show eighths of an inch. Carpenters and tradesmen use the architect’s rod. Surveyors and engineers use the engineer’s rod. The rod reading by the blue arrow is one foot, four and one eight of an inch. (1’ 4 1/8”)

## Slide 12: Engineer’s Rod
Measures in decimal feet.
Red numbers show number of feet.
Black numbers show tenths of a foot.
Top and bottom of each line represents one hundredth of a foot.
Notes: Read the engineer’s rod in tenths and hundredths of a foot. The number of feet are red in color and the tenths have graduated marks by a number in black. Smaller graduated marks represent hundredths of foot. The rod reading by the blue arrow is 5.36 feet.

## Slide 13: References
Jacobs, C. O., & Mattox, K. E. (1988). Leveling and land measurement practices for agriculture. Tucson, AZ: Department of Agricultural Education, University of Arizona.
Koel, L., & Mazur, G. A. (2013). Agricultural technical systems and mechanics. Orland Park, IL: American Technical Publishers.