## Slide 2: Scale Drawings
Agricultural Power and Technology
Unit 4 – Lesson 4.1 Making a Plan

## Slide 3: Types of Drawings
Pictorial sketch
Floor plan
Isometric drawing
Orthographic drawing
Sectional drawing
Notes: There are many types of drawings used in agricultural mechanics. Each serves a different purpose and provides a unique view of a structure or object. Sketches are freehand drawings used to quickly inform a technician and are not to scale. A floor plan provides an overhead view of an object and is most commonly used to show the features of a room such as walls, windows, appliances, and furniture. Isometric drawings show a three-dimensional aspect of an object, while an orthographic drawing will show multiple two dimensional sides. A sectional drawing is used when internal parts of an object cannot be seen from an external view.

## Slide 4: Pictorial Sketch
Shows three dimension at once.
Not drawn to scale.
Dimensions indicate length, width, and height.
Height
Length
Width
Notes: A pictorial sketch will show dimensions, but will not be to scale.

## Slide 5: Floor Plan
Drawn to scale
Overhead view
Includes dimensions of walls, doors, windows, furniture, and appliances
Notes: A floor plan provides an overhead view of a building that shows dimensions and features of rooms.

## Slide 6: Isometric Drawing
Similar to a pictorial drawing.
Isometric drawing shows all three dimensions at once.
Horizontal lines are drawn at 30° angles.
  The view becomes distorted because of the 30° angle.
30°
Notes: Isometric drawings provide a three-dimensional view that is slightly distorted due to the angles of the horizontal lines.

## Slide 7: Orthographic Drawing
Shows one side at a time.
May look very different than the three-dimensional object.
The number of views needed will depend upon the complexity of the object.
Left Side
Front
Top
Right Side
Notes: Orthographic drawings show a two dimensional view of an object. The shape of the object will determine the number of sides that need to be drawn.

## Slide 8: Sectional Drawing
Sectional drawings display internal parts of an object that cannot be seen from a traditional view.
Side View
Top view
Cross Sectional Side view
Notes: Sectional drawings show a cross section of the object to reveal internal features. This cross sectional drawing shows a hole drilled in the cube. The depth of the hole would not be known without using a cross sectional view.

## Slide 9: Plan Components
Border Line
Title Block
Drawing
  Object Lines
  Dimensional Lines
  Dimensions
NAME | PROJECT NAME | SCALE | DATE
Front or side
Top
End
8”
12”
30”
8”
Example Plan
Notes: The drawing is one component of a plan for constructing an object. Other components include a border line and title block. A border line is heavy line drawn ½ inch in from the outer edges of the paper. A title block ½ inch in height is drawn above the lower border. The object in the plan is drawn to scale using multiple times of lines and dimensions.

## Slide 10: Title Block
Name of person who made drawing
Title of drawing
Scale of drawing
Date
Located in lower right corner of drawing ½ inch above border line.
All letters are capitalized.
JIMMY OLSEN | DAILY PLANET | 1’=1/4″ SCALE | 12/15/14
Notes: All drawings contain a title block. The title block informs the reader what the drawing is, its scale and who drew it.

## Slide 11: Types of Lines
Object lines
  Thick lines defining the objects shape.
Hidden lines
  Shows hidden features that cannot be seen from the outside.
Dimension lines
  Shows size or location of an object in a drawing.
Center point
  Locates center points of arcs and circles.
Notes: Different types of lines are used to interpret the drawing and understand the locations of the objects features.

## Slide 12: Lines
Dimensional Line
Object Lines
Notes: Dimensional lines will have arrows pointing towards lines that indicate where the measurement begins and ends. Object lines may or may not have dimensional lines.

## Slide 13: Lines
Center Point
Hidden Lines
Notes: The center point indicates the center of the pipe in the drawing. The hidden line shows that the opening of the pipe goes through the entire base of the object.

## Slide 14: Reading Dimensional Information
Not all dimensions may be given in a drawing.
All dimensions can be calculated with the information provided in a drawing.

## Slide 15: Dimensional Question
What is the inside diameter of the pipe?
  Inside radius = 2 1/2″
  Diameter = 2 x radius
  Inside diameter = 5″
Notes: The internal diameter and external radius of the pipe can be calculated using the information provided in the drawing.

## Slide 16: Dimensional Question
What is the external radius of the pipe?
  External radius = External diameter/2
  External radius = 6″/2
  External radius = 3″

## Slide 17: References
Herren, R. (2006). Agricultural mechanics fundamentals and applications. (5th ed.). Clifton Park, NY: Thomson Delmar Learning.
Koel, L., & Mazur, G. A. (2013). Agricultural technical systems and mechanics. Orland Park, IL: American Technical Publishers.