## Slide 2: Welding
Agricultural Power and Technology
Unit 4 – Lesson 4.3 Fasten and Fuse

## Slide 3: What is Welding?
Process of fusing metal together by melting material into a molten puddle using a heat source and filler material.
The Lincoln Electric Company
Notes: Welding fuses material together to form a strong permanent joint between material. It is most commonly used to fuse metals together, but is also applied to plastics.

## Slide 4: Safety Requirements
Welding requires specialized PPE and equipment
  Leather gloves
  Welding helmets
  Leather aprons
  Ventilation
  Welding curtains
  Cooling buckets
The Lincoln Electric Company
Notes: Welding requires specialized personal protective equipment to protect the welder from high heat and intense light emitted during the welding process. Leather gloves and aprons are worn to protect the welder from heat. All skin must be covered and a shaded face shield worn to protect it from the intense infrared rays. Welding areas need to be well ventilated to protect the welder from toxic fumes and cooling buckets should be available to cool the welded metal.

## Slide 5: Common Heat Sources
Electrical
  Electricity arcs on metal producing a high concentration of heat which melts the metal.
Gas
  Flammable mixture of gases produces a flame with a high temperature capable of melting metal.
The Lincoln Electric Company
Notes: Welding uses a source of heat to fuse the metal together. High electrical current or flammable mixture of gasses are used to create a high heat source that will melt the metal.

## Slide 6: Filler Metal
Filler metal is added to the molten puddle to change the mechanical properties of the weld.
Filler metals vary based upon the type of welding.
The Lincoln Electric Company
Notes: Filler metal is added to the molten puddle to increase the strength of the weld and change the mechanical properties of the metal. Some welds need more strength where others need to be more ductile and able to bend. Some filler metals have a flux coating on them that produces a gas during the welding process to protect the weld from impurities. The flux will also form a coating on the weld called slag that protects the weld as it cools.

## Slide 7: Welding Technique
Each welding process requires special technique.
Many factors influence weld quality.
Movement of puddle
Speed of welder
Intensity of heat
Size of molten puddle
Distance heat source is from metal.
The Lincoln Electric Company
Notes: There are many factors that will effect the quality of the weld. The angle of the filler metal and its distance from the base metal will affect the size and shape of the weld. The weld is also dependent upon the intensity of the heat and the movement of the heat source along the joint being welded.

## Slide 8: Weld Defects
Welds are defective when proper technique is not used.
Splatter
No penetration
Incorrect width
Porous
The Lincoln Electric Company
Notes: If the welding technique is incorrect, a defective weld will be produced. Welders are able to look at a weld and determine the cause of the defect. Poor technique and practice will cause welds to be porous and weak with no penetration.

## Slide 9: References
Herren, R. (2006). Agricultural mechanics fundamentals and applications. (5th ed.). Clifton Park, NY: Thomson Delmar Learning.
Koel, L., & Mazur, G. A. (2013). Agricultural technical systems and mechanics. Orland Park, IL: American Technical Publishers.