## Slide 2: Hydraulic Power
Agricultural Power and Technology
Unit 5 – Lesson 5.3 Mechanical Energy

## Slide 3: Hydraulic Principles
Hydraulic systems work because of the properties of liquids.
Liquids have no shape of their own.
Liquids will not compress.
Liquids transmit equal pressure in all directions.
Notes: Hydraulic systems are based upon the properties of liquids. Because liquids cannot be compressed, they will transfer the same amount of force that is applied to them in all directions.

## Slide 4: Hydraulic Systems
Use a liquid under pressure to transfer energy in an enclosed space.
Consists of three components
  Source of energy
  Pathway
  Load
Notes: Hydraulic systems use a pressurized liquid to apply a force to do work, such as move or lift an object.

## Slide 5: Energy Source and Pathway
Energy Source
  Hydraulic pump that moves fluid to apply force.
Pathway
  Hoses and valves provide a path for fluid to flow.
Notes: A hydraulic system has an energy source that applies pressure throughout the system. The pressure is transferred through a hose to a load where the pressure will apply force to a piston in a cylinder to do work.

## Slide 6: Hydraulic Load
Load
  Hydraulic cylinder applies force to lift an object.
  The force applied to the piston of the cylinder must be greater than the load.
Notes: The pressure in the system applies a force to the system greater than the force of the object. Therefore, the object will move.

## Slide 7: Pressure
The pressure in a system is equal to the force applied by the energy source divided by the surface area where the force is applied.
Notes: The pressure is equal to the force divided by the surface area of the piston.

## Slide 8: Surface Area
The pistons in the cylinder are circular in shape.
Find the area of a piston by multiplying the radius squared times pi (π)
Pi (π) = 3.14
Radius
Notes: The area of the piston can be found by calculating the radius, which is half of the diameter, squaring the radius and multiplying times Pi.

## Slide 9: Source Pressure
If the energy source applies 8lbs of force to a 2in2 area, 4lbs/in2 of pressure is in the system.
Notes: Once the force and area is known, the pressure in the system can be calculated.

## Slide 10: Pascal’s Law
Pascal’s Law states that the pressure exerted in fluid system is equally applied throughout the entire system.

## Slide 11: Load Force
The force applied to the load is equal to the pressure in the system times the surface area of the load piston.
Notes: The pressure is applied throughout the entire system. The force applied to the load is equal to the pressure applied by the source times the surface area of the piston applying force to the load.

## Slide 12: Load Force
If 4lbs/in2 of pressure is a applied to a 3in2 cylinder, 12lbs of force is transferred to the load.
Notes: The 4lbs of force applied from the source is able to apply 12lbs of force to the load.

## Slide 13: References
Buriak, P., & Osborne, E. (2006). Power Systems. In J. Lee (Ed.), Physical Science Applications in Agriculture. Danville, IL: Interstate.
Koel, L., & Mazur, G. A. (2013). Agricultural technical systems and mechanics. Orland Park, IL: American Technical Publishers.