## Slide 2: Simple Machines
Agricultural Power and Technology
Unit 6 – Lesson 6.1 Machine Design

## Slide 3: What is a Simple Machine?
A device for altering the magnitude or direction of force.
Transfers mechanical energy throughout a machine to do work.
No machine can create energy.
Machines only transfer the energy or transform the energy.
Notes: Simple machines change or multiply a force.

## Slide 4: Work
Simple machines perform work measured in joules.
Work input = work output
Work = force x distance
Input (force x distance) = Output (force x distance)
Notes: Simple machines perform work. The work put into a machine is equal to work output of machine. Because work is equal to force times distance, the force times the distance of the input side of a machine is equal to force times distance of the output side of the machine.

## Slide 5: Friction
Work in a machine is equal if there is no friction.
No machine is 100% efficient.
Work input is always equal to or greater than work output.
Notes: Friction reduces the amount work output, resulting in energy lost in the from of heat. Because of friction, machines are not 100% efficient. There will be more work put into a machine than what is produced by the machine.

## Slide 6: Lever
A rigid bar pivots on a fulcrum.
Output force is greater than input force in the lever below.
If input force is 2N and 5cm from the fulcrum and the output force is 5N and 2cm from the fulcrum, work is equal.
Notes: No work has been created with the lever. The input force times the distance the input force is to the fulcrum will be equal to the output force times the distance the load is from the fulcrum. The input force is less than the output force because of the distance it is from the fulcrum. Each side of this lever has a total of 10 joules of work. 2N x 5cm = 5N x 2cm.

## Slide 7: Inclined Plane
Used to reduce the force required to lift an object.
The object will travel a further distance on an inclined plane and require less force.
Notes: An inclined plane can be used to lift an object. Even thought the force needed to move the object decrease, the distance increases. Therefore the work to move the object would be the same as lifting it if there is no friction.

## Slide 8: Wedge
A combination of two inclined planes that can be used to separate material.
Notes: Wedges are used to cut and separate material.

## Slide 9: Wheel and Axle
A wheel is a continuous lever that pivots around a fulcrum.
The radius of the wheel is the distance of the lever.
The fulcrum is the center of the axle.

## Slide 10: Screw
A combination of a inclined plane, wedge, and wheel and axle.
An inclined plane is wrapped around a cylinder.
Converts rotary motion into a linear motion.
Notes: You learned in Lesson 4.3 Fasten and Fuse, that screws are an example of an inclined plane combined with a wedge and a wheel and axle. The screw bites into the material pulling itself in as it is turned. The screw can hold two or pieces of material together.

## Slide 11: Pulley
Wheel and axle
Changes direction of a force
Reduces output force required to do work
Notes: Pulleys are a wheel and axle used to change the direction of an applied force. A system of pulleys can reduce the input force needed to lift an object.

## Slide 12: Gears
Wheel and axle with wedge shaped teeth called cogs.
Teeth mesh together with one gear controlling the other.
Multiple gears can be connected to adjust speed, direction, and torque.
Notes: A gear consists of a wheel and axle with wedge shaped teeth called cogs. The cogs of a gear interlock with cogs of another gear. Because they are interlocked, if one gear moves the other will move as well. Gears of different sizes can control the speed, direction, and amount of torque in a machine.

## Slide 13: References
Buriak, P., & Osborne, E. (1996). Power Systems. In J. Lee (Ed.), Physical science applications in agriculture. Danville, IL: Interstate.
Hewitt, P., Suchocki, J., & Hewitt, L. (2010). Conceptual physical science explorations (2nd ed.). Glenview, IL: Pearson.