## Slide 2: Precision Systems
Mechanical Systems in Agriculture
Unit 1 – Lesson 1.2 Agricultural Production

## Slide 3: Precision Agriculture
Collect georeferenced data with GPS
GIS analyzes data and answers production questions
Calibrate machines for input rates
Use GPS and guidance systems to apply inputs
Systematic approach to site-specific agricultural management
Notes: Precision agriculture involves the integration of GPS, GIS, and guidance systems to collect data, calculate inputs, and calibrate and operate agricultural equipment. All systems work together on a farm operation to optimize a farmer’s efficiency and increase their profitability.

## Slide 4: Precision Systems
Global Position Systems (GPS)
  Geographic locations
Geographic Information Systems (GIS)
  Spatial database
Guidance Systems
  Assisted and automated navigation
Notes: Precision systems used in agriculture include GPS, GIS, and guidance systems. GPS is used to identify specific geographic locations. GIS provides information about specific locations. Guidance systems assist equipment operators in navigating equipment efficiently.

## Slide 5: Global Positioning System
System of satellites and receivers
Determine exact locations and elevations on the earth
http://ardupilot.org/rover/_images/gps_satellite_constellation.jpg
Notes: Global positioning systems consist of satellites and receivers. Satellites surrounding the earth send signals to GPS receivers. GPS receivers process the signals to determine the location. Receivers can be handheld or mounted on equipment, such as tractors and combines. Accuracy of receivers vary. Handheld receivers can predict locations within a few feet. Receivers on equipment can predict locations within inches.

## Slide 6: GPS in Agriculture
Identify locations of land features
  Fences
  Boundaries
  Buildings
  Roads
  Soil samples
Navigation
https://commons.wikimedia.org/wiki/File:John_deere_8345_rt.jpg
Notes: GPS is used in agriculture to identify precise locations of features, such as field boundaries and fences. GPS receivers on equipment work with navigational systems that can direct equipment to drive to specific locations or follow geographic lines. GPS is also used when collecting data for input into a geographic information system. Geographic locations of soil and yield samples are examples of features that are marked with a GPS for later analysis with GIS.

## Slide 7: Geographic Information Systems
Electronic map
Visual data representation
Georeferenced data
Identifies and analyzes spatial relationships
Notes: GIS is georeferenced data stored in a database that can be displayed as an electronic map. Georeferenced data is data associated with a specific geographic location. The database stores the locations of features, such as roads and bridges, along with a description of those features called attributes. The number of attributes describing a location is endless. GIS can analyze the data to answer questions about spatial relationships of features. Example questions include.
Which field has the highest yield potential for corn?
What is the total acreage of the pasture and length of fencing surrounding it?
How much fertilizer will need to be added to the field to grow wheat?
What is the relationship between last year’s crop yield and the pH of the soil?

## Slide 8: GIS Data
Base layer
Vectors
  Shapefiles (.shp)
  Points
  Lines
  Polygons
Continuous data
  Rasters
  Contour
Vector Map
Raster Map
Contour Map
Notes: Most GIS maps have a base layer with an aerial image used for referencing the location of the data. GIS data is presented in the form of vectors and continuous data. Vectors are coordinate based data representing specific points, lines, or polygons. Continuous data is specified data where any location within an area represents a specific value. Examples of continuous data include rasters, and contour lines. Rasters are equally sized areas while contours will vary in size. The raster map is an example of a yield map. Each colored dot on the yield map represents the predicted yield for that area. The contour map is an example of a pH map showing the soil pH of the field. Each color represents a different soil pH.

## Slide 9: Variable Rate Technology
Vary input rates based upon GIS data
Inputs
  Herbicide – kill weeds
  Fertilizer (i.e. nitrogen) – feed plants
  Lime – raise soil pH
Requires equipment with GPS and variable rate sensors
Notes: GIS can be used to vary the rate of crop inputs. Once a farmer has information about his or her field, such as weed location, fertility, or soil pH, he or she can vary the input based upon location. Herbicide can be sprayed only where weeds are located. Nitrogen can be applied where soil fertility is low. Lime can be applied where soil pH is low. Specialized application equipment combined with GPS is needed to vary input rates on the field.

## Slide 10: Guidance Systems
Light bar
Automated navigation
Advantages
  Limit overlaps
  Avoid skips
  Save on inputs
    Fuel
    Herbicide
    Fertilizer
    Lime
Notes: Guidance systems used in agriculture assist operators traveling across a field. They help the driver travel in a straight line and ensure the entire field is treated with the correct amount of an input. Guidance systems help operators save fuel by optimizing the distance and time they spend operating the tractor. Guidance systems save on other input costs by reducing overlaps and preventing skips.

## Slide 11: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 12: References
Brase, Terry. (2006). Precision agriculture. Clifton, NY: Thomson Delmar Learning.
ESRI. (n.d.) Gis dictionary. Retrieved from https://support.esri.com/en/other-resources/gis-dictionary/browse/
John Deere. (n.d.). John deere guidance systems: guidance you can grown with. Retrieved from https://m.deere.com/common/docs/products/equipment/agricultural_management_solutions/guidance_systems/brochure/en_GB_yy1114823_e.pdf