## Slide 2: Programmable Controls
Mechanical Systems in Agriculture
Unit 2 – Lesson 2.2 Electrical Systems

## Slide 3: Programmable Logic Controller
A device using microprocessors to control machines or processes
Components
  Inputs
  Outputs
  Controls
Notes: Technicians program programmable logic controllers (PLCs) to operate machines and equipment based upon data collected by sensors. PLC’s are found in many agricultural machines and facilities even though you may not see them. PLC’s can turn on heating and cooling operations, alert operators of danger, and direct the movement of equipment. The three major components of a PLC are inputs, outputs, and controls.

## Slide 4: Inputs
Data collecting sensors
Data read by the controller
Example data
  Temperature
  Moisture
  Humidity
Notes: Sensors collect data from a PLC’s surroundings. Data collected from a facility or machine used in agriculture could include temperature data in a greenhouse, moisture data in a grain dryer, or humidity in an animal barn. During this lesson, you will use a temperature senor to collect data.

## Slide 5: Outputs
Machines
  Motor
  Heater
  Light
  Alarm
Notes: Outputs are the controlled machines doing the work. The control will power the machines when the data from the sensor fits the programed description. Example outputs include lights, motors, ventilation systems, and alarms. You will use the model outputs shown on the slide to develop your prototype systems.

## Slide 6: Controls
Control the output based upon collected data and the program
Regulate electrical power made available to the machine
Vernier Digital Control Unit (DCU)
Notes: Controls are the devices programmed to manage machines based upon sensor data. You will program a DCU during this lesson. The DCU can manage electrical current to three outputs. The current is managed by writing programs.

## Slide 7: Simple Threshold Logic
Program used to control a machine with a single statement
If–then statement
If the temperature is greater than 85F, then turn on the fan.
Notes: A simple threshold logic statement is used to turn on or off a machine using a single statement and a single data point. The example shows a program to activate line 1 if the temperature in the facility is greater than or equal to 85 degrees Fahrenheit. Line 1 could be attached to a fan or air conditioning unit to cool the facility.

## Slide 8: Compound Logic Statement
Used to control machines under various conditions
Three functions
  UNTIL - Time based or allow cycling
  AND - Set a range of conditions
  OR - Set varying conditions
Notes: Compound logic statements control machines using multiple statements and data points. This allows the machine to operate under a variety of conditions. If an operator wanted to turn on the cooling system when it reached 85 degrees, but wanted the system to cool the facility UNTIL the temperature was 75 degrees, a compound logic statement could be used. AND statements can set a specific data range for the machine to operate in. OR statements allow to set varying conditions or data ranges to operate a machine.

## Slide 9: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 10: References
Vernier (2015). Vernier digital control unit (dcu). Beaverton, OR: Author.