## Slide 2: Governor and Ignition
Mechanical Systems in Agriculture
Unit 3 – Lesson 3.2 Disassembly Required

## Slide 3: External Governor Parts
Regulates engine speed
Governor control lever
Governor arm
Governor spring
Governor linkage
Copyright Briggs and Stratton Corp. Used with permission
Notes: The governor control lever controls the movement of the arm. The spring controls how much force is needed to move the arm. The linkage closes the throttle plate when the arm moves. Before disassembling the governor, use a marker to mark the holes where springs and linkages are connected. Note the direction and position of the springs (loop up or down) and record the position of the wiring beneath the governor arm.

## Slide 4: Pinch Bolt
Pinch bolt holds the arm in place on governor shaft
Governor will not work if the pinch bolt is not tight
Copyright Briggs and Stratton Corp. Used with permission
Notes: Move the governor back and forth. Note how the lever is connected to the shaft which goes into the crankcase of the engine. If the hole on the governor arm where the pinch bolt attaches becomes out of round, the governor arm should be replaced.

## Slide 5: Speed Control Bracket
Fastened by two screws of different lengths
Connects red ground wire of ignition system
Copyright Briggs and Stratton Corp. Used with permission
Notes: Check screw lengths. One may be shorter than the other. If so, use a permanent marker to mark where each came from. Note the red ground wire bolted to the engine block.

## Slide 6: Blower Housing
Contents
  Rewind starter
  Electrical switch
Purpose
  Covers flywheel
  Covers ignition system
  Filters debris from air as it enters
Copyright Briggs and Stratton Corp. Used with permission
Notes: The blower housing contains multiple components essential to engine operation.

## Slide 7: Switch Wiring
Copyright Briggs and Stratton Corp. Used with permission
Notes: Switch wiring needs to be disconnected from the electrical switch on the blower housing. Engines with a low oil sensor module have a 3 terminal rocker on/off switch. The switch terminals are numbered. Mark each terminal so they can be reinstalled in the correct order. Sketch the wire routing near governor shaft.

## Slide 8: Armature
Magneto passes under the armature
Builds up and releases electrical current
Distance between magneto and armature must be 0.010”
  Measure air gap using a feeler gauge or Briggs and Stratton ruler.
Copyright Briggs and Stratton Corp. Used with permission
Notes: The magnet on the flywheel rotates and passes under the armature. The magnet passes electrical current through the armature which is released as a spark from the spark plug. TEACHER NOTE: Demonstrate how to properly use a feeler gauge to measure the air gap. Then show how the Briggs and Stratton ruler is designed to set the air gap for the armature.

## Slide 9: Oil Module
Stops the engine by grounding electrical current when oil level is low
Connected to a finger guard
Copyright Briggs and Stratton Corp. Used with permission
Notes: The oil module is attached to the finger guard. Remove finger guard. Do not remove the module from the guard. The module delays the engine from shutting down if the oil level temporarily changes due to the engine being tipped or moved.

## Slide 10: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 11: References
Blake, Jay. (2014). 130G32 PowerPoint® teardown. Retrieved from http://www.thepowerportal.com/nA/English/BriggsStratton/TrainingResources/Iwanttoteach/EngineTeardowns.htm