## Slide 2: Internal Components
Mechanical Systems in Agriculture
Unit 3 – Lesson 3.2 Disassembly Required

## Slide 3: Flywheel
Turns the crankshaft
Crankshaft attached to piston camshaft
Momentum of heavy flywheel keeps engine running
  Use flywheel strap to remove
  Flywheel Video
Copyright Briggs and Stratton Corp. Used with permission
Notes: Remove the flywheel nut using a 21mm socket and breaker bar. Hold the flywheel in place using a flywheel strap. The flywheel has fins to circulate air to cool the engine. The magneto (strong magnet) is attached to the flywheel and is part of the ignition system. The flywheel’s heavy mass provides momentum to keep the engine running. Teacher Note: Play flywheel removal video from The Power Portal for students.

## Slide 4: Crankcase Cover
Contains bearings for crankshaft and camshaft
Gasket seals the joint between cover and crankcase
Copyright Briggs and Stratton Corp. Used with permission
Notes: Remove the crankcase cover and crankcase gasket. The crankcase houses the oil to lubricate the engine. The gasket seals the cover and crankcase to prevent oil leaks. Bearings in the cover hold the crankshaft and cam shaft in place. There are two dowels connecting the crankcase cover to the crankcase, be sure they do not fall out and become lost.

## Slide 5: Cam Gear
Timing marks of cam gear and crankgear gear align
Ratio of cam gear to crankgear gear is 1:2
  Cam gear rotates once for every two rotations of crankgear
Copyright Briggs and Stratton Corp. Used with permission
Notes: The crank gear rotates the cam gear. The cam gear has a shaft with lobes attached. The lobes open and close the valves. The gears need to be “timed” correctly so valves open and close during the correct event.

## Slide 6: Cam Gear and Tappets
Cam lobes move tappets and connecting rods to open valves.
Compression release system on cam shaft reduces force needed to start engine.
Copyright Briggs and Stratton Corp. Used with permission
Notes: Observe the shape of the lobes. The compression release system on the backside of the cam gear increases the size of the lobe when first starting the engine. The larger lobe keeps a valve slightly open, reducing compression and allowing the engine to be easily pull started by the operator.

## Slide 7: Piston/Connecting Rod Assembly
Piston and rod have alignment marks called “match marks”
Rod cap has an oil sling designed to splash oil throughout the engine.
Copyright Briggs and Stratton Corp. Used with permission
Notes: The piston and connecting rod can only be installed in one direction. The rod cap has marks to direct the technician on how it should be connected to the rod.

## Slide 8: Crankshaft
Converts linear motion to rotary motion
PTO side of crankshaft
Copyright Briggs and Stratton Corp. Used with permission
Notes: The crankshaft converts linear motion of piston into rotational motion. The end of the crankshaft, called the power take off is connected to mower blades, pulleys, belts, pumps and generators to do work. Use caution during removeal. Be careful not to scratch bearing surfaces. The flywheel key slot on the PTO side is very sharp and can cut your hand.

## Slide 9: Piston Rings
Prevent oil from entering combustion chamber
Keep compression in combustion chamber
Rings are very brittle
DO NOT REMOVE RINGS
Copyright Briggs and Stratton Corp. Used with permission
Notes: Piston rings seal the combustion chamber from the crankcase. Each ring is designed to either lubricate the bore walls or increase compression in the combustion chamber. Rings are removed using a ring expander. Rings are brittle and expensive to replace. Carefully observe the ends of the rings to see the cross sectional shape. Be sure the oil ring does not overlap during reassembly.

## Slide 10: Crankcase
Houses the oil
Sealed with gaskets
Contains low oil sensor
Governor gear and shaft
  Governor thimble behind lever
Copyright Briggs and Stratton Corp. Used with permission
Notes: The crankcase has an oil sensor to shut off engine if oil is too low. A plastic governor gear is connected to a governor shaft, which moves the governor arm and controls the engine speed. There is a plastic thimble that goes over the shaft. Be careful not to lose it. The thimble can fall off during reassembly. You will need to check the governor assembly before attaching the crankcase cover.

## Slide 11: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 12: References
Blake, Jay. (2014). 130G32 powerpoint teardown. Retrieved from http://www.thepowerportal.com/nA/English/BriggsStratton/TrainingResources/Iwanttoteach/EngineTeardowns.htm