## Slide 2: Starting the Teardown
Mechanical Systems in Agriculture
Unit 3 – Lesson 3.2 Disassembly Required

## Slide 3: Organization
Keep small bolts, screws and nuts in plastic bags.
Label bags so you know where the parts go when you begin reassembling your engine.
Store all parts, bags and engine in a storage tote.
Notes: You will need to stay organized by storing and labeling all parts.

## Slide 4: Documentation
Briggs and Stratton OHV repair manual
Advanced Product Service Information
Notes: The Briggs and Stratton OHV repair manual has assembly instructions for the engine. Use the manual to see how parts are assembled. The Advanced Product Service Information (APSI) has updated info for new models that have had changes made to the basic assembly. The APSI also has specifications and torque information for measuring and reassembling the engine.

## Slide 5: OHV Manual
OHV manual has assembly procedures.
Torque or Specification | Manual Location |  | 
 | Sec. | Page | Fig.
 | 2 | 16 | 8
Notes: Document where to find information about each step you complete. Include the section, page and figure number.

## Slide 6: Advanced Product Service Information
Step | Hardware | Tools | Torque or Specification | Manual Location |  | 
 |  |  |  | Sec. | Page | Fig.
Remove air cleaner base | 1 8mm screw 2 10mm nuts Air cleaner base | 8mm socket 10mm socket | 8mm - 40lb-in 10mm – 50lb-in | 2 | 13 | 2
Notes: Use the APSI to find torque and specifications about the engine.

## Slide 7: Air Filter
Removes particles from air before air enters carburetor
Inspect filter for tears and replace if present
Foam pre-filter is washable if equipped
Copyright Briggs and Stratton Corp. Used with permission
Notes: The first component to remove from the engine is the air filter. The air filter prevents dirt from entering the engine and wearing components. Do not use compressed air to clean a paper cartridge. The pressurized air could make holes in the paper. Clean the cartridge by gently tapping the paper cartridge on a hard service. Replace the cartridge if extremely dirty or soaked in gas or oil. Wash dirty pre-filter with water and dish soap. Wring and let dry before reinstalling.

## Slide 8: Trim Panel
Covers throttle
Remove using 8mm socket
Copyright Briggs and Stratton Corp. Used with permission
Notes: Keep all parts organized by storing in separate containers or sealable bags and labeling them. The 8mm screws found on the trim panel look similar to other screws but are designed for a specific use.

## Slide 9: Breather Tube and Gaskets
Exhaust gases move from valve cover to the air filter.
Gaskets provide tight seal between air cleaner and carburetor
Copyright Briggs and Stratton Corp. Used with permission
Notes: The breather is found under the valve cover. It allows gases to leave the engine but not reenter. The tube directs the gases to the air cleaner where the air is recycled back into the engine. Recycling the air decreases pollutants expelled into the air by the engine.
Disconnect the breather tube before removing the air cleaner backing plate. Inspect gaskets for tears and note how the gaskets fit on the air cleaner backing.

## Slide 10: Fuel Line Disconnection
Remove line from tank or carburetor
Use pliers and fuel line pry tool
Copyright Briggs and Stratton Corp. Used with permission
Notes: NOTE: Demonstrate to students how to use the pry tool to remove the fuel line from the fuel tank. Remove the pinch clamp using a pliers. Hold the fuel line with the pliers while using the pry tool to push the tubing off the connection.

## Slide 11: Fuel Tank
Fastened with two 12mm nuts and one 8mm screw
There may still be fuel in the fuel line. Watch for leaks when line is disconnected
Copyright Briggs and Stratton Corp. Used with permission
Notes: Remove the fuel tank and hose. The tanks is a specially designed reservoir for fuel. The cap allows air to be vented. The tank is designed to allow fuel to run off the outside and contains baffles to prevent sloshing in the inside. Have a storage container available to drain excess fuel from the fuel tank. Outlet nipple on the fuel tank contains a fuel filter. Remove and clean the filter if it is clogged.

## Slide 12: Carburetor
Connected to the governor via linkage and spring
Linkage closes the throttle plate
Spring pulls the throttle plate open
Carburetor
Copyright Briggs and Stratton Corp. Used with permission
Notes: Note how the choke and throttle plate of the carburetor are controlled. The governor spring should be holding the throttle plate in an open position. The governor linkage pulls on the governor plate causing the plate to close.

## Slide 13: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 14: References
Blake, Jay. (2014). 130G32 PowerPoint® teardown. Retrieved from http://www.thepowerportal.com/nA/English/BriggsStratton/TrainingResources/Iwanttoteach/EngineTeardowns.htm