## Slide 2: Drive Systems
Mechanical Systems in Agriculture
Unit 4 – Lesson 4.3 Agricultural Processing

## Slide 3: Synchronous Drive Systems
Consist of gears, sprockets and chains
Have a positive engagement between drive and driven sides
No slippage between parts
Gearbox
Notes: Synchronous drives work similar to pulley systems, which are non-synchronous drives. Synchronous drives have a direct connection between all parts. When one part moves in a synchronous drive, the other parts must move because of the positive connection. Non-synchronous belt systems do not have a positive connection and can slip. Chains, sprockets, and gears are all examples of synchronous drives and may be combined together in a drivetrain.

## Slide 4: Chain Drive
Uses chain to transfer power between sprockets
Chain meshes with sprocket teeth
Chain components
  Roller
  Pin
  Links
Notes: Chain drives are used where gears are unable to mesh together to drive parts. A chain has interconnected links that fit around a toothed sprocket. All sprockets connected to a single chain will rotate in the same direction. Roller chains links are connected using rollers and pins.

## Slide 5: Bevel Gear
Gear boxes with shafts at right angles or 90 degrees
Teeth tapered to mesh together
Miter gear
  Same size bevel gears intersecting
Notes: Bevel gears have tapered teeth that fit together at a 90 degree angle changing the direction the drive shaft is facing.

## Slide 6: Worm Gear
Large speed reductions
Worm – screw thread
Worm gear – spur gear
Change direction of the drive by 90 degrees or a right angle
Notes: Worm gear systems are used for large speed reductions and smooth operations. The worm is the drive gear transferring power to the spur gear (driven gear).

## Slide 7: Rack and Pinion
Spur gear - circular
Rack gear - linear
Converts rotary motion to linear motion
Notes: A straight rack gear driven by a rotating spur gear converts rotary motion into a linear motion.

## Slide 8: Tracks and Conveyors
Conveyors move material from one place to another
  Driven by synchronous and non-synchronous drives
Track systems – used in place of wheels to increase traction and decrease soil compaction
Notes: Synchronous systems can drive conveyors transporting material or power tracks that mobilize equipment such as tractors and combines.

## Slide 9: Cams
Change rotary motion to linear motion
Small engine cams
  Rotating objects
Face cam
  Lever attached to face of rotating component such as a gear or sprocket
Notes: Cams transmit motion using irregular shapes on external or internal surfaces. You assembled external cams used to open and close valves on a small engine. Internal cams, such as a face cam, can be found on the face of a gear or sprocket.

## Slide 10: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 11: References
Koel, L., & Mazur, G. A. (2013). Agricultural technical systems and mechanics. Orland Park, IL: American Technical Publishers.