## Slide 2: Pneumatic Components
Mechanical Systems in Agriculture
Unit 4 – Lesson 4.3 Agricultural Processing

## Slide 3: Fluid Power Systems
Pneumatic – use compressed gas
  Compressor
  Hoses
  Actuators
  Valves
Hydraulic – use compressed liquid
  Pump
  Hoses
  Actuators
  Valves
Notes: Pneumatic and hydraulic systems us fluid to transfer power within a machine. Components are very similar and operate the same way.

## Slide 4: Pneumatic Systems
Uses
Power tools
  Wrenches
  Nail guns
Factory automation
  Manufacturing
  Processing
  Packaging
Advantages
Clean
High torque with low speed
Limited moving parts
Fewer breakdowns
Notes: Pneumatic systems have a wide array of uses in industry and have some of the same advantages over other types of mechanical systems.

## Slide 5: Compressor Components
Accumulator
Fluid storage reservoir
Pressurized
Regulator
Controls flow at constant pressures
Pressure gauge
Measures pressure in system
Notes: Pneumatic systems use compressors to create the pressure within the system. The compressed air is stored in a reservoir tank called an accumulator. A valve called a regulator controls the pressure of the fluid released into the system. The images in the slide show a physical example of an accumulator and regulator you will use during this lesson.

## Slide 6: Compressor Schematics
Accumulator
Regulator
Pressure Gauge
Notes: Specific images and shapes are used to represent pneumatic components in a drawing called a schematic. The systems you will construct in this lesson will have a separate accumulator, regulator, and pressure gauge represented by the symbols shown in this slide.

## Slide 7: Actuators
Linear motion
  Single acting
  Double acting
Rotary motion
  Motor
Produce motion from another form of energy
Double Acting Cylinder
Notes: The two main types of actuators in a pneumatic system are motors and cylinders. The two common cylinders are double acting and single acting. Double acting have fluid controlling extension and retraction of the cylinder rod. A single acting cylinder has fluid controlling one direction and a load such as a weight or spring controlling the other direction.

## Slide 8: Cylinder Schematics
Single acting
spring return
Double acting cylinder
Notes: Review the schematic symbols for cylinder types shown on the slide. Note the short lines on top of the cylinders representing the ports for hose connections. A single acting cylinder uses air pressure for linear movement in one direction and another type of force such as gravity or a spring in the other direction. A double acting cylinder’s extension and retraction movements are controlled by air pressure.

## Slide 9: Valves
Direction of fluid
  Check valve
  Directional valve
Amount of fluid
  Flow control valve
Pressure of fluid
  Regulator
Notes: Valves control the direction, flow, and pressure of fluid in a system. A valve’s internal passages guide air in the direction need to control a cylinder or motor.

## Slide 10: Valves
Check valves
Allow flow in one direction
Flow control valves
Control the rate of fluid flow
Allow flow in one direction
Notes: Check valves allow fluid movement in one direction. Flow control valves limit the flow of fluid moving in the system.

## Slide 11: Directional Control Valves
Redirect fluid flow in a system
Four components
  Valve actuators
  Positions
  Ports
  Ways
Notes: Directional control valves have four main components. The valve actuator on the valve changes the internal position of the passageways. The positions of a valve are defined by the number of combinations the passageways can be. The ports and ways are the places where air can flow into and out of a valve.

## Slide 12: Directional Control Valve Actuators
Valve actuators activate a valve and change direction of fluid flow.
  Push button
  Solenoid
  Internal pilot
  Spring
Notes: Four types of valve actuators are push buttons, springs, solenoids, and internal pilots. Push buttons require action by an operator to move the valve. Solenoids use electro-magnetic current to move a switch controlling a valve. Air flow through an internal pilot can move a valve as well. Springs are used for an automatic return after a load is released such as an operator’s hand on a button, discharge of electrical current in a solenoid, or release of air pressure in an internal pilot. Valves can have more than one actuator. The valve shown here has a solenoid and a spring operating the valve.

## Slide 13: Valve Positions
Represented by flow boxes on a schematic
Two or three positions
Schematics show hoses connected to the active flow box
Two Positions
Three Positions
Notes: The valve actuator moves the valve into different positions which redirects the fluid. Most valves have two positions. The push-button spring-activated valve shown in the slide has two positions. The position closest to the button shows the flow of air when the button IS pushed, and the spring is compressed. The position closest to the spring shows the flow of air when the button is NOT pushed, and the spring is extended. The position closest to the spring is considered the active position and is where lines representing hoses connect on a schematic.

## Slide 14: Valve Ports
Number of end points in a flow box
Connections or exhausts
1
2
3
4
2
3
1
Three hose attachments and one exhaust
Two hose attachments and one exhaust
Notes: Ports on a schematic represent where hoses can attach or air can be exhausted to the atmosphere. Some schematics will show a short line extending from the flow box indicating where a hose can attach or a triangle indicating where no hose attaches and air is exhausted to the atmosphere. The two-position, push-button, spring-activated, valve is a four-port valve with three ports for hose attachments and one exhaust port. The two-position, dual-solenoid, valve has three ports. One exhaust and two ports for hoses.

## Slide 15: Valve Ways
Number of ways air can enter or exit a valve
1
2
3
4
1
1
2
3
Two-position, push-button, spring-return, four port, four-way valve
Two-position, duel solenoid, three port, three-way valve
Notes: Valves are also describe by the number of ways fluid can enter or exit a valve. In most instances, the number of ports is equal to the number of ways air can flow through a valve. The two-position, push-button, spring-return, four-port valve has four ways air can enter and exit the system. The two-position, dual-solenoid, three-port valve has three ways for air to enter or exit.
Exceptions to the rule occur when two ports share the same exhaust function. Even if there are two exhausts, the fluid is going to the same destination.

## Slide 16: Example Fluid Flow
1 Inlet
2 Outlets
1 Exhaust
Spring Activated Position
Push Button Activated Position
Notes: Fluid can only flow through one of the two positions. In the schematics above you can see how air always enters and exhausts through the same ways no matter the position of the valve. However, the pressurized air (red line), and exhaust air (blue line) change when the button is activated.

## Slide 17: Naming a Valve
Two position, push-button, spring-return, four-port, four-way valve
Two position, double solenoid, three-port, three-way valve
Notes: It is important to de as detailed as possible when describing a valve so a technician knows the exact valve to order or purchase. The description should include the number of positions, type of actuators, number of ports, and number of ways.

## Slide 18: Practice
Three-position, double-pilot, five-ported, four-way valve
Practice naming the valve.
Notes: Practice naming the valve.
The valve has three positions.
Two pilots activate the valve.
Each position has five ports.
There are four ways for air to flow in and out (the two exhausts have the same purpose and therefore are only counted once).

## Slide 19: Presentation Review
Mark or highlight three key points
List two ideas or concepts related to previous knowledge.
List questions you have about this topic.
Keep notes organized and available for use throughout the course.

## Slide 20: References
Automation Direct. (2017). Understanding circuit symbols. https://www.automationdirect.com/pneumatics/misc/circuit_symbols
National Fluid Power Association. (2017). Fluid power advantages. http://www.nfpa.com/fluidpower/fluidpoweradvantages.aspx