## Slide 1: Hematology Week 11
Seminar

## Slide 2: Week 10 Quiz
Review

## Slide 9: Week 11 Content
Review

## Slide 10: Hematology Manual and Special Testing
Selected topics: Chapter 31
Chapter 32
Lynn Jones, BS, MT, ASCP
Assistant Program Director
Christina A Nevel-McGarvey, PhD, MS, MT(ASCP)
Professor, Clinical Laboratory Sciences

## Slide 11: Specimen Collection
Pre-analytical Steps
  Patient identification
  Requisition Verification
  Biosafety
Venipuncture
  Most commonly from median cubital vein in arm
  Vacutainer tubes containing Ethylene diaminetetraacetic acid (EDTA) anticoagulant
Capillary Puncture
  Finger or heel

## Slide 12: Microhematocrit (Hct) Tubes
Heparinized tubes for capillary blood
Non heparinized tubes for EDTA collected blood
Sealing clay

## Slide 13: Finger Stick using Capillary Tube

## Slide 14: Microhematocrit Centrifuge Systems
Balance tubes
Centrifuge 5 min, at 14,500 rpm

## Slide 15: Hct After Centrifugation
Read packed red cell volume using microhematocrit reader
Do not include buffy coat
Hematocrit is reported as % rbc to total blood volume
Normals
  Newborn: 53-65%
  Infant: 30-43%
  Adult male: 42-52%
  Adult female: 37-47%

## Slide 16: RBC Indices
Red blood Cell Indices
  Measurements that describe the size and hemoglobin content of red blood cells. Used to detect and monitor Anemia.
Mean Corpuscular Hemoglobin (MCH)
  A measurement of the average weight of hemoglobin in a red blood cell.
Mean Corpuscular Hemoglobin Concentration (MCHC)
  The measurement of the average concentration of hemoglobin in a red blood cell.
Mean Corpuscular Volume (MCV)
  A measure of the average volume of a red blood cell.
Red Cell Distribution Width (RDW)
  A measure of the variation in size of red blood cells

## Slide 17: RBC Indices
The calculations:-
  MCV = hematocrit ÷ rbc count x 10
  MCH = hemoglobin ÷ rbc count x 10
  MCHC = hemoglobin ÷ hematocrit x 100
The ASCP usually has one or two index calculations on the exam

## Slide 18: Manual Cells Counts
Hemocytometer
  2 square-ruled areas separated by an H shaped moat
  Must use standardized coverslip
  Depth of chamber is 0.1mm
  Counting area is 3mm x3mm

## Slide 19: Unopette System
Ensures precise dilution and charging of sample
  Calibrated micropipette
  Sealed diluent reservoir
    RBC will be lysed for WBC and Platelet Count
  Pipet shield/puncture tool

## Slide 20: Unopette Replacements

## Slide 21: Charging the Hemocytometer

## Slide 22: Microscopic Counting!

## Slide 23: Neubauer Ruling
WBC
Count 4 corner Primary Squares
RBC
Count 5 secondary squares in center primary square
Triple Boundary Lines-
  Count all cells within squares including those touching middle line
Double Boundary Lines-
  Count all cells within square and those touching innermost line

## Slide 24: Don’t count dead cells or cells touching the lower & right boundary line!

## Slide 25: Proper charging and distribution of cells is of utmost importance in accurate counting!

## Slide 27: Red Blood Cell Count
RBC/mm3 = #RBC Counted x Depth factor x Dilution Factor
Area
  Depth factor = 10
  Dilution factor =200
  Area=0.2
Therefore, we can formulate to a factor of 10,000
Example: Counted 600 Cells
600 x 10,000 = 6.0 x 106/mm3 or 6.0 x 1012/L
Normals:
  Newborn 4.4--5.8 x 1012/L
  Infant/Child 3.8--5.5 x 1012/L
  Adult Male 4.7--6.1 x 1012/L
  Adult Female 4.2--5.4 x 1012/L

## Slide 28: White Blood Cell Count
WBC/mm3 = #WBC Counted x Depth factor x Dilution Factor
Area
  Depth factor = 10, Dilution factor =100, Area=4
Therefore, we can formulate to a factor of 250
Example: Counted 50 Cells
50 x 250 = 12.5 x 103/mm3 or 12,500/ml
Normals:
  Newborn 9,000--30,000/ml
  1 week old 5,000--21,000/ml
  1 month old 5,000--19,500/ml
  6-12 months 6,000--17,500/ml
  2yrs 6,200--17,000/ml
  Child/Adult 4,800--10,800/ml

## Slide 29: Platelet Count
Count ALL 25 squares of the Center Primary Square
Platelets /mm3 = #Platelets x Depth factor x Dilution Factor
Area
  Depth factor = 10
  Dilution factor =100
  Area= 1.0
Therefore, we can formulate to a factor of 1,000
Example: Counted 200 Platelets
200 x 1,000 = 200 x 103/mm3 or 200,000/ml or 200 x 109/L
Normals:
  Normal 150,000—450,000/ml

## Slide 30: Preparing a Manual Smear
Many whole blood determinations require preparation of a manual smear with properly distributed cells a short distance inward from the feathered edge

## Slide 31: Reticulocyte Unopette

## Slide 32: Reticulocytes: Giemsa vs. Supravital Stain
Polychromasia
Precipitate of RNA & organelles

## Slide 33: Reticulocyte Reporting
Recticulocyte Count= #Retics x 100
1000
Corrected Reticulocyte Count= %Retic x Patient Hct%
45%
  Compares patient Hematocrit with Normal Hematocrit
Absolute Reticulocyte Count= %Retic x RBC count
100
  Multiply by RBC Count to convert to Absolute Retic Value
Reticulocyte Production Index (RPI)=
%Retic x patient Hct% / 45%
Reticulocyte maturation time at the patient Hct
  Accounts for presence of Shift, takes into account corrected retic count and maturation time of retics based upon patient Hct

## Slide 34: Reticulocyte Normals
Reticulocyte Count
  Newborn= 2.6—6.0%
  Adult = 0.5—2.0%
Absolute Reticulocyte Count= 24—80 x 109/L
RPI = 3 or greater
Maturation Time for Reticulocytes
  45% Hct = 1 day
  35% Hct = 1.5 days
  25% Hct = 2 days
  15% Hct = 3 days

## Slide 35: Kleihauer-Betke/ Acid Elution for Fetal Hemoglobin/K-B
Peripheral blood smear is exposed to acidified buffer before staining
  Fetal hemoglobin does not elute
  Other hemoglobin elute from cells
  Fetal cells stain bright red
Staining of postpartum maternal blood for identification of percentage of fetal cells present.
  Determine possible fetal maternal hemorrhage in the newborn
  Assess the magnitude of fetal maternal hemorrhage to calculate dosage of Rh immune globulin to be administered.
Staining of peripheral blood to aid in diagnosis of certain types of anemia
  Ex. Hereditary Persistence of Fetal Hemoglobin (HPFH)

## Slide 36: Detection of Hemoglobinopathy: Sickle Solubility Kits

## Slide 37: Sickle Solubility Test
RBC are lysed by surfactant
Released hemoglobin is reduced by sodium hydrosulfite
Hemoglobin A is soluble
  See through the tube
Hemoglobin S is insoluble
  Cannot see through tube

## Slide 38: Determination of Hemoglobinopathy: Hemoglobin Electrophoresis
RBC lysate applied to electrophoretic support and proteins separated by charge.
Acid and alkaline buffers produce different banding patterns to analyze after protein staining.

## Slide 39: Hemoglobin Analysis via Electrophoresis & Densitometry

## Slide 40: Automated Hemoglobin Analysis - HPLC

## Slide 41: Separation of Hemoglobin Variants HPLC

## Slide 42: HPLC- Beta Thalassemia

## Slide 43: Osmotic Fragility Test
Determines resistance of RBC to hemolysis in varying concentrations of hypotonic saline at room temperature
Increased Osmotic Fragility
  Hereditary Spherocytosis
  Thalassemia
  Sickle Cell Anemia

## Slide 44: Osmotic Fragility Curve

## Slide 45: Increased Osmotic Fragility
Spherocytes
Thalassemia

## Slide 46: Ham’s Test
Detects RBC Membrane Defects
Diagnostic for Paroxysmal Nocturnal Hemoglobinuria (PNH)
Patient RBC exposed to normal serum and patient’s serum, both acidified to pH 6.5—7.0
Acid activates complement in serum and lyses PNH cells
Controls include heat inactivated serum and normal RBC

## Slide 47: Sugar Water Test
Detects RBC Membrane Defects
Diagnostic for Paroxysmal Nocturnal Hemoglobinuria (PNH)
Sucrose provides low ionic strength
This promotes complement binding to RBC’s resulting in hemolysis

## Slide 48: Erythrocyte Sedimentation Rate (ESR)
Inflammation changes the proteins in and surrounding red blood cells
This causes RBC to bind to one another in clumps, making them denser than normal RBC
An ESR test simply measures the rate which RBC sink to the bottom of a test tube
The faster the RBC fall, the more inflammation is present in the body

## Slide 49: Arterial Blood Gases-ABG’s
2-3 ml arterial blood must be collected in a sealed anaerobic syringe with small amount of heparin, placed on ice
Automated Analysis
Measures Acid/Base status and respiratory gases in the arterial blood
  pH, pCO2, pO2 (and HCO3)
  paO2 measures oxygen saturation, overall adequacy of gas exchange
  paO2 affected by altitude and age of patient
  Normal paO2 = 70-100 mm Hg
  ppO2 is measured with pulseoximeter

## Slide 50: Arterial Blood Gases
pH
  The measure of how acidic or basic the blood is
  Normal pH 7.35—7.45
  Lower pH = Acidosis
  Higher pH = Alkalosis
pCO2
  The pressure of carbon dioxide gas dissolved in blood
  It tells us how much breathing we are doing
  Normal CO2 = 35—45 mmHg
  Less breathing=moreCO2=More Acid=Lower pH
  More breathing = less CO2=Less Acid=Higher pH
HCO3
  How much bicarbonate is dissolved in the blood
  It is a buffer that combines with acid and decreases its ability to lower pH
  Kidneys control pH by excreting or retaining bicarbonate
  Normal HCO3 = 22—26 mEq

## Slide 51: Using Acid-Base Map to Analyze Arterial Blood Gases

## Slide 52: Arterial Blood Gas Analysis
pH tells you if the blood gas will be acidotic, alkalotic or normal.
The CO2 and HCO3 together tell you why the pH is like it is. The total range of your choices in the interpretation of blood gases is contained in the following list:
  Normal
  Respiratory Alkalosis
  Metabolic Alkalosis
  Respiratory Acidosis
  Metabolic Acidosis
  Combined Respiratory and Metabolic Alkalosis
  Combined Respiratory and Metabolic Acidosis
  Partially Compensated Respiratory Alkalosis
  Partially Compensated Metabolic Alkalosis
  Partially Compensated Respiratory Acidosis
  Partially Compensated Metabolic Acidosis
  Compensated Respiratory Alkalosis
  Compensated Metabolic Alkalosis
  Compensated Respiratory Acidosis
  Compensated Metabolic Acidosis

## Slide 53: Example of using Acid-Base Map to interpret ABG Analysis
The pH of 7.24 is in the acidosis region, as is the HCO3 of 16. The CO2 of 37 is normal. This tells us that the acidosis is not respiratory, but metabolic in origin : A METABOLIC ACIDOSIS

## Slide 55: Blood Gases Report

## Slide 56: ABG Reference Ranges

## Slide 57: Automated Hematology Technology BAYER Flow Cytometric Instrument

## Slide 58: Automated Cytometric Methodology
Cells pass through laser beam
Laser light scatter is measured
Cell size is measured
Cell surface markers can be detected with tagged markers
Cells can be separated into populations

## Slide 59: Beckman Coulter Counter Instrumentation

## Slide 60: WBC Histogram

## Slide 61: RBC Histogram Showing 2 RBC Populations

## Slide 62: WBC Scattergram with RBC Histogram

## Slide 63: Platelet Histogram

## Slide 64: 5 Part Automated Differential

## Slide 65: Scattergram

## Slide 66: Bayer Scattergram

## Slide 67: VCS Technology
Volume
Physically measure the volume that the entire cell displaces in an isotonic diluent. This method accurately sizes all cell types regardless of their orientation in the light path.

## Slide 68: VCS Technology
Conductivity
Alternating current in the radio frequency (RF) range short circuits the bipolar lipid layer of a cell's membrane, allowing the energy to penetrate the cell. This powerful probe is used to collect information about cell size and internal structure, including chemical composition and nuclear volume.

## Slide 69: VCS Technology
Scatter
When a cell is struck by the coherent light of a LASER beam, the scattered light spreads out in all directions. Using a proprietary new detector, median angle light scatter (MALS) signals, are collected to obtain information about cellular granularity, nuclear lobularity and cell surface structure.

## Slide 70: VCS Technology
Simultaneous Measurements
VCS is the only single channel analysis that uses 3 independent energy sources working in concert with each other. These three measurements are taken simultaneously.

## Slide 71: VCS Technology
Distinct cell clusters
Software analyzes these clusters for:
Quantity: in %
Position: indicates morphology
Density: cell populations
Deviation of these clusters from their normal quantity, shape, position or density are an indication of a distributional or morphological abnormality.
A comprehensive set of flags is used to point the medical technologist toward the most likely cause of these abnormalities.

## Slide 72: Manual Cell Counter

## Slide 73: Clinical Laboratory Scientist

## Slide 74: What type of cells do you see?

## Slide 75: Proficiency Testing! What is this?

## Slide 76: Be sure to keep reviewing your Atlas of Hematology!

## Slide 77: End Week 11…. But week 12 Discussion topics next!

## Slide 78: Week 12 Discussion Topic A
Topic A: Which of the topics that were covered in this course did you find the easiest and most difficult to understand?
~Identify the specific week(s) in which the easiest and most difficult topic(s) arose.
~Identiy the specific topic(s).
~Why do you think that you found the identified topics easier than other topics which arose in the course?
~Why do you think that you found the identified topics more difficult than other topics which arose in the course?
~For the topics that you found most difficult in this course, it is very important to have a plan in place to make sure that you fully understand these topics before moving on to more difficult topics. What plan do you have in place to accomplish this?

## Slide 79: Week 12 Discussion Topic B
Topic B: Which of the topics that were covered in this course do you predict will be most applicable to the area of clinical laboratory science that you intend on pursuing?
~Identify the specific week(s) in which the topic(s) arose.
~Identify the specific topic(s).
~Identify the specific area of clinical laboratory science that you would like to specialize in.
~Make relevant connections between the identified topic(s) and the area of clinical laboratory science that you would like to specialize in.