## Slide 1: Penis

## Slide 2: Objectives:
Upon completion of this presentation, students will be able to:
Identify the anatomy and blood supply of the penis.
Describe the function of the penis.
Recognize the normal sonographic appearance.
Distinguish the different pathologies of the penis.

## Slide 3: ANATOMY
Root
Body
  Corpora cavernosa x2
  Corpus spongiosum x1
    Contains the urethra
  Tunica albuginea
    Fibrous tissue bounds and separates 3 corpora
Glans penis
Buck’s fascia
  Thick covering of skin enveloping the penis

## Slide 4: ARTERIES
Internal Iliac Arteries
Internal Pudendal Arteries
Dorsal Artery
Cavernous Artery
  supplies corpora cavernosa
Bulbourethral Artery
  supplies corpus spongiosum, glans penis, and urethra

## Slide 5: VEINS
Superficial Dorsal Vein
  Located outside of Buck’s fascia
Deep Dorsal Vein
  Beneath Buck’s fascia
Pudendal Venous Plexus
Internal Pudendal Vein

## Slide 6: BLOOD SUPPLY

## Slide 7: FUNCTION
Eject semen
  Stimulation increases blood supply
  Expansion of arteries, cause compression of veins
  Built up pressure causes bladder sphincter to close during ejaculation

## Slide 8: SONOGRAPHIC APPEARANCE
Corpora Cavernosa
  Paired
  Symmetrically round or oval
  Homogenous
  Medium-level echoes
Corpus spongiosum
  Homogenous
  Medium-level echoes
Tunica albuginea (septum penis)
  Echogenic

## Slide 9: SONOGRAPHIC APPEARANCE

## Slide 10: SONOGRAPHIC APPEARANCE

## Slide 11: PATHOLOGY

## Slide 12: PEYRONIE’S DISEASE
Calcified or fibrous tissue deposited in the dorsal penis
Can cause the penis to bend
Becomes painful when erect
Extent defined by ultrasound

## Slide 13: PEYRONIE’S DISEASE
EVALUATION:
  High frequency linear array
  The patient or another sonographer hold the penis
  May scan ventral or dorsal side

## Slide 14: PEYRONIE’S DISEASE
Hyperechoic areas in peripheral margin, may shadow

## Slide 15: STRICTURE
Urethra becomes narrowed
Develops due to trauma or infection
Sonography determines the length and width of stricture
Seen when urethra distended with fluid

## Slide 16: STRICTURE
Sonourethrography
EVALUATION:
  High frequency linear array
  Patient needs distended urethra
    Urine
    Sterile Saline
    Lidocaine gel
  Long and transverse views obtained
  Measure length and width of stricture

## Slide 17: SONOGRAPHIC APPEARANCE
Thickened urethral wall
Decreased lumen

## Slide 18: IMPOTENCE
Inability to achieve or maintain erection
Causes:
  Poor arterial flow
    Inadequate systolic flow indicates arterial insufficiency
  Venous leak
    Venous blood leaks out during erection

## Slide 19: IMPOTENCE (cont’d)
EVALUATION:
  Scan from ventral side
  First scan with penis flaccid
    Measure diameter and flow of cavernosal arteries
    Doppler angle less than 60 degrees and matching direction of flow
    Measure peak systolic and end-diastolic velocities
  Vasodilator injected into cavernosum
  Measure diameter and velocities every 5 minutes until erection stops

## Slide 20: IMPOTENCE (cont’d)
Cavernosal peak systolic arterial velocity >30 cm/sec is normal
Cavernosal systolic arterial velocity<25 cm/sec after injection = poor arterial flow
Cavernosal end-diastolic flow at 15-20 min after injection > or = 5 cm/sec, indicates venous incompetence
  Surgically corrected

## Slide 21: IMPOTENCE

## Slide 22
https://youtu.be/X2tubB7Sxlk